## Slide 1: Computer Architecture & Organization
CPIT 201

## Slide 2
  Computer Subsystems
        CPU
        Memory
        I/O subsystems
  Subsystems Interconnections
        Connecting CPU and memory
        Connecting I/O devices
  Program Execution
  Different Architectures
        CISC
        RISK
Chapter Outline
        Pipelining
        Parallel processing

## Slide 3: Getting Started
Organization is how features are implemented (Transparent to the programmer)
  How does a computer work?
  Control signals, circuit design, memory types.
Architecture is those attributes visible to the programmer
  How do I design a computer?
  Instruction set, number of bits used for data representation, I/O mechanisms, addressing techniques.
  Each family of computers shares the same basic architecture and organization differs between different versions

## Slide 4: Computer Subsystems

## Slide 5: Computer Subsystems
Three broad categories make up a computer:
  CPU (Central Processing Unit)
  Main Memory
  I/O (Input / Output) subsystems
Storage Devices

## Slide 6: Computer Subsystems
  CPU (Central Processing Unit)
  The CPU performs operations on data. It consists three parts:
  ALU (Arithmetic Logic Unit)
  CU (Control Unit)
  Set of Registers

## Slide 7: Computer Subsystems
  CPU (Central Processing Unit)
  ALU (Arithmetic Logic Unit)
    It performs logic, shift & arithmetic operations on data.
  CU (Control Unit)
    It controls the operation of each subsystem. Controlling is achieved through signals sent from the control unit to other subsystems.
  Set of Registers
    Registers are fast stand-alone storage locations that hold data temporarily.

## Slide 8: Computer Subsystems
  CPU (Central Processing Unit)
  Set of Registers
    Multiple registers are needed to facilitate the operation of the CPU. They are categorized into three groups:
    Data Registers
      Dozens of registers to hold the intermediate results from operations.
    Instruction Registers (IR)
      Program is made of instructions to run by a computer… Instructions of a program are loaded to instruction registers to be called by CU.
    Program Counter (PC)
      It keeps tracking of the instruction currently being executed. After execution of the instructions, the counter is incremented to point the address of the next instruction in memory.

## Slide 9: Computer Subsystems
  Main Memory
  It consists of a collection of storage locations, each with a unique identifier, called an address.
  Data is transferred to and from memory in groups of bits called words. A word can be a group of 8 bits, 16 bits, 32 bits or 64 bits (and growing).
Address
Contents
(values)

## Slide 10: Computer Subsystems
  Main Memory
  Address space
    To access a word in memory, it requires an identifier. Each word is identified by an address. The total number of uniquely identifiable locations in memory is called the address space.
    For example, a memory with 64 kilobytes and a word size of 1 byte has an address space that ranges from 0 to 65,535.
Notes: just think of it as your thinking space, how much you can think about at once without writing something down:) thats what ram is to a computer

## Slide 11: Computer Subsystems
Notes: In mathematics, the binary logarithm (log2 n) is the power to which the number 2must be raised to obtain the value n. ... For example, the binary logarithm of 1 is 0, the binary logarithm of 2 is 1, the binary logarithm of 4 is 2, and the binary logarithm of 32 is 5. The binary logarithm is the logarithm to the base 2.

## Slide 12: Computer Subsystems
  Main Memory
  Address space
  This table assists to know the exact number of bytes.

## Slide 13: Computer Subsystems
  Main Memory
  Memory types can be classified into three types:
  RAM (Random Access Memory)
    SRAM (Static RAM)
    DRAM (Dynamic RAM)
  ROM (Read Only Memory)
    PROM (Programmable read-only memory)
    EPROM (Erasable programmable read-only memory )
    EEPROM (Electrically erasable programmable read-only memory)
  Cache memory

## Slide 14: Computer Subsystems
  Main Memory
  RAM (Random Access Memory)
    It makes up most of the main memory. It hold data as long as power is on. It has two types based on its design:
DRAM (Dynamic RAM) | SRAM (Static RAM)
Uses capacitors | Uses flip-flop gates
Its cells need to be refreshed periodically because capacitors lose some of its charge with time | Data stored as long as the power is on there is no need to refresh memory locations
Slow but inexpensive | Fast but expensive.
used for a computer's main memory | Typically used for CPU cache
T-RAM ?
Z-RAM ?

## Slide 15: Computer Subsystems
  Main Memory
  ROM (Read Only Memory)
    It is written by the manufacturer & the CPU can read from. It is not like RAM, data on ROM is not lost when the power is off. One example of data that ROM keeps is boot program that runs when computer switched on. It can be found in three types:
    PROM (Programmable read-only memory)
    EPROM (Erasable programmable read-only memory )
    EEPROM (Electrically erasable programmable read-only memory)

## Slide 16: Computer Subsystems
  Main Memory
  Cache memory
    Cache memory is faster than main memory, but slower than the CPU and its registers. Cache memory, which is normally small in size, is placed between the CPU and main memory. The CPU always check first the cache.

## Slide 17: Computer Subsystems
  Main Memory
  Memory hierarchy
    Very fast and inexpensive memory is not always possible to satisfy. A compromise needs to be made. The solution is hierarchical levels of memory.

## Slide 18: Computer Subsystems
  Input / Output subsystem
  The collection of devices referred to as the input/output (I/O) subsystem. This subsystem allows a computer to communicate with the outside world and to store programs and data even when the power is off. Input/output devices can be divided into two broad categories:
  Non-storage devices
  Storage devices

## Slide 19: Computer Subsystems
  Input / Output subsystem
  Non-storage devices
    They allow the CPU/memory to communicate with the outside world, but they cannot store information.
      Keyboard & monitor
      Printer
  Storage devices
    They store large amounts of information to be retrieved at a later time. They are cheaper than main memory, and their contents are nonvolatile—that is, not erased when the power is turned off. They are sometimes referred to as auxiliary storage devices. They can be categorized to:
      Magnetic devices (e.g. Hard Disk)
      Optical devices (e.g. CD)

## Slide 20: Subsystems Interconnections

## Slide 21: Subsystems Interconnections
  Information needs to be exchanged between the three subsystems (CPU, Memory, and I/O).
  The three subsystems have to communicate.
  How these three subsystems are interconnected?
    CPU and memory connections
    CPU and I/O connections

## Slide 22: Subsystems Interconnections
  Connecting CPU and memory
      The CPU and memory are normally connected by three groups of connections, each called a bus:
    Data bus
    Address bus
    Control bus

## Slide 23: Subsystems Interconnections
  Connecting CPU and memory
  Data bus
    It is made of several connections, each carrying 1 bit at a time. The number of connections depends on the size of the word used by the computer
      E.g. 32 bits word  32 data buses
  Address bus
    It allows access to a particular word in memory. The number of connections depends on the address space of the memory. If the memory has words, the address bus need to carry bits at a time  connections are needed.

## Slide 24: Subsystems Interconnections
  Connecting CPU and memory
  Control bus
    It carries communication between CPU & memory.
        E.g. there must be a code from CPU to memory to specify
        a read or write operation.
    The number of connections depends on the total number of control commands a computer needs. If a computer has control actions  connections are needed. bits can define different operations.

## Slide 25: Subsystems Interconnections
  Connecting I/O devices
  I/O devices cannot be connected directly to the buses that connect the CPU and memory, because the nature of I/O devices is different from the nature of CPU and memory.
  I/O devices are electromechanical, magnetic, or optical devices, whereas the CPU and memory are electronic devices.
  I/O devices also operate at a much slower speed than the CPU/memory.
  There is a need for some sort of intermediary to handle this difference. Input/output devices are therefore attached to the buses through input/output controllers or interfaces.

## Slide 26: Subsystems Interconnections
  Connecting I/O devices

## Slide 27: Subsystems Interconnections
  Connecting I/O devices
  Two types of controllers can be found
    Serial  one data connection, moving bits in serials.
    Parallel  several data connections, moving bits in blocks.
Common kinds of I/O controllers |  | 
SCSI (Small Computer System Interface) | FireWire | USB (Universal Serial bus)
Parallel | Serial | Serial
Need terminator | high speed devices | High/low speed devices
Few devices number | Up to 63 devices | Up to 127 devices

## Slide 28: Subsystems Interconnections
  Connecting I/O devices
  In the following photo,
  what type of controllers
  the I/O devices use?

## Slide 29: ……

## Slide 30: References
  Forouzan, B. & Mosharraf, F. (2008), Foundations of Computer Science, Second Edition, Thomson Learning.