## Slide 1: Operations on Data
CPIT 201

## Slide 2
  Logic Operations
        Logic Operations at bit level
        Logic Operations at pattern level
  Shift Operations
        Logical Shift
        Circular Shift
        Arithmetic Shift
  Arithmetic Operations
        Integers in two’s complement format
        Integers in sign-and-magnitude format
        Reals in floating-point format
Chapter Outline

## Slide 3: Getting Started
An electronic computer is made up of a number of circuits.
Each circuit can be designed using the rules of Boolean algebra, {True/False = 1/0}
The basic elements of circuits are called logic gates.
A gate is an electronic device that operates on a collection of binary inputs and produces a binary output.
Notes: http://www.csd.uwo.ca/faculty/lila/logic/logicgates.pdf

## Slide 4: Logic Gates

## Slide 5: Logic Gates
A logic gate is an idealized or physical device implementing a Boolean function; that is, it performs a logical operation on one or more logical inputs, and produces a single logical output.

## Slide 6: Logic Gates
Logic gates
AND OR
NOT XOR

## Slide 7: Logic Gates
The AND gate
  It accepts two or more inputs and produces one output
  It outputs ‘0’ when minimum one input is ‘0’
  It outputs ‘1’ when both inputs are ‘1’
Output | Input | 
A.B | B | A
0 | 0 | 0
0 | 1 | 0
0 | 0 | 1
1 | 1 | 1
Notes: http://www.technologystudent.com/elec1/dig2.htm

## Slide 8: Logic Gates
The AND gate
  E.g. safe use of machines
Notes: http://www.technologystudent.com/elec1/dig6.htm

## Slide 9: Logic Gates
The OR gate
  It accepts two or more inputs and produces one output
  It outputs ‘0’ when both inputs are ‘0’
  It outputs ‘1’ when minimum one input is ‘1’
Output | Input | 
A+B | B | A
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
1 | 1 | 1
Notes: http://www.technologystudent.com/elec1/dig2.htm

## Slide 10: Logic Gates
The inverter gate
  The inverter accepts a Boolean value as input and produces the complement of this value as its output
  It outputs ‘0’ when the input is ‘1’
  It outputs ‘1’ when the input is ‘0’
Output | Input
Ā | A
1 | 0
0 | 1

## Slide 11: Logic Gates
The XOR gate
  It accepts two or more inputs and produces one output
  It outputs ‘0’ when the inputs are the same
  It outputs ‘1’ when the inputs are different
  This gate is a combination of the previous three gates (NOT, AND, OR)
    [x AND (NOT y)] OR [(NOT x) AND y]
Output | Input | 
AB | B | A
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1

## Slide 12: Logic Gates
Combinations of gates
  Combinatorial circuits can be constructed using a combination of inverters, OR gates and AND gates.
  When combinations of circuits are formed, some gates may share inputs.
  One method is to use branchings to indicate all the gates that use a given input.
  The other method is to indicate this input separately for each gate.
  Note that output from a gate may be used as input by one or more elements.
Notes: http://www.csd.uwo.ca/faculty/lila/logic/logicgates.pdf

## Slide 13: Logic Gates
Combinations of gates

## Slide 14: Logic Gates
Combinations of gates
  E.g. Logic circuit for a simple house alarm
Notes:   http://www.technologystudent.com/elec1/dig5.htm

## Slide 15: Logic Gates
Combinations of gates
  E.g. Logic circuit for a simple house alarm
1
Notes:   http://www.technologystudent.com/elec1/dig5.htm

## Slide 16: Logic Gates
Combinations of gates
  E.g. control street lights
Notes:   http://www.technologystudent.com/elec1/digq3.htm

## Slide 17: Logic Gates
Combinations of gates
  E.g. control street lights
Notes:   http://www.technologystudent.com/elec1/digq3.htm

## Slide 18: Logic Gates
Build a circuit that attends a teacher if:
  LAB door is opened using key & computer is turned on
  OR LAB door is opened using figure print

## Slide 19: Logic Gates
Build a circuit that attends a teacher if:
  LAB door is opened using key & computer is turned on
  OR LAB door is opened using figure print

## Slide 20: Logic Gates
Build a circuit that (for safety reason) does not allow a user to use a microwave and an oven at the same time.

## Slide 21: Logic Gates
Build a circuit that (for safety reason) does not allow a user to use a microwave and an oven at the same time.

## Slide 22: Logic Gates
Gates with multiple inputs

## Slide 23: Logic Gates
Gates with multiple inputs
  E.g. suspicious behaviour in an office = Alarm Sounds
    Light is OFF
    Door is opened
    Drawer is opened

## Slide 24: Logic Gates
Bitwise operations
  A bit string is a sequence of 0s and 1s (bits). The length of the string is the number of bits in the string.
  We can extend bit operations to bit strings. We define bitwise OR, bitwise AND and bitwise XOR of two strings of the same length to be the strings that have as their bits the OR, AND and XOR of the corresponding bits in the two strings.
  Hexadecimal numbering system may be used for the purpose of short representation.
    E.g. 2F AND 71  0010 1111 AND 0111 0001
2 F 7 1

## Slide 25: Logic Gates
Bitwise operations
  E.g. Find the bitwise AND, bitwise OR, bitwise XOR, and bitwise NOT

## Slide 26: Logic Gates
Bitwise operations
  In the combination of logic gate below, find the outputs C, D and E of the inputs A and B.

## Slide 27: Logic Gates
Bitwise operations
INPUT |  |  | OUTPUT |  | 
A | B |  | C | D | E
1 | 1 |  | 1 | 0 | 1
1 | 0 |  | 0 | 1 | 1
1 | 0 |  | 0 | 1 | 1
1 | 1 |  | 1 | 0 | 1
1001
0110
1111
AB⨁
A AND B XOR (NOT B)
Notes: http://spmphysics.onlinetuition.com.my/2013/07/logic-gates-combination-of-logic-gate.html

## Slide 28: Shift Operations

## Slide 29: Shift Operations
In shift operations bits are moved by one or more bit positions within a register,' either to the left or to the right.
  Depending on the data-type of the word under consideration, there are actually three different kinds of shifts:
Shift Operations
Logical Shift
Arithmetic Shift
Circular Shift (Rotate)
signed number
in two’s complement
Notes: http://research.microsoft.com/en-us/um/people/gbell/Designing_Computers_and_Digital_Systems/00000104.htm

## Slide 30: Shift Operations
Logical Shifting is applied to a pattern of unsigned number.
  For the left shifting, the leftmost/ MSB(Most Significant Bit) bit is lost and ‘0’ is inserted to the rightmost bit.
  For the Right shifting, the rightmost/ LSB(Least Significant Bit) bit is lost and ‘0’ is inserted to the leftmost bit.
Logical left shift one bit
Logical right shift one bit
Most Significant Bit
Least Significant Bit
Notes: This operation is not used for arithmetic, but might be used to isolate a field of bits (contiguous set of bits).
https://en.wikipedia.org/wiki/Logical_shift

## Slide 31: Shift Operations
Circular Shifting (Rotate) is same as logical shifting applied to a pattern of unsigned number. However, in circular shifting bits are rotated, no bits are lost or introduced in the shifting process.
Left circular shift
Right circular shift
Notes: It can be used for encryption
https://en.wikipedia.org/wiki/Circular_shift

## Slide 32: Shift Operations
Arithmetic shift assume that the bit pattern is a signed integer in two’s complement format.
  Arithmetic left shift is equivalent to multiplying by a power of 2.
  Arithmetic right shift is equivalent to dividing by a power of 2.
Left arithmetic shift by 1 empty position in the rightmost bit is filled ‘0’
Right arithmetic shift by 1 The empty position in the leftmost is filled with a copy of the original
Notes: https://en.wikipedia.org/wiki/Arithmetic_shift

## Slide 33: Shift Operations
Arithmetic shift left
  A sign reversal occurs if the bit leftmost changes in value after shift.
  This happens if the multiplication by 2 causes an overflow
  An overflow flip-flop can be used to detect an arithmetic shift-left overflow.
▲Before the shift, if the leftmost two bits differ, the shift will result in an overflow.
Notes: http://slideplayer.com/slide/8521028/

## Slide 34: Shift Operations
Examples
Result | Operation | Input
00010100110 | Logic right shift (3 bits) | 10100110
10100110000 | Logic left shift (3 bits) | 10100110
11010100 | Right rotate (3 bits) | 10100110
00110101 | Left rotate (3 bit) | 10100110
11110100110 | Arithmetic right shift (3 bit) | 10100110
10100110000 | Arithmetic left shift (3 bit) | 10100110

## Slide 35: Shift Operations
Result | Operation | Input
00010100110 | Logic right shift (3 bits) | 10100110
10100110000 | Logic left shift (3 bits) | 10100110
11010100 | Right rotate (3 bits) | 10100110
00110101 | Left rotate (3 bit) | 10100110
11110100110 | Arithmetic right shift (3 bit) | 10100110
10100110000 | Arithmetic left shift (3 bit) | 10100110
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1
▲in arithmetic right shift we do not move the 3 bits at one time because the sign bit (leftmost) needs to be preserved for every shifting process. That’s why you notice three 1s added to the left.
 | Right shift by 3
Right Shift by 1 | 
Right Shift by 1 | 
Right Shift by 1 | 

## Slide 36: Arithmetic Operations

## Slide 37: Arithmetic Operations
Arithmetic operations involve adding, subtracting, multiplying and dividing. We can apply these operations to integers and floating-point numbers.
The focus, in this course, is on adding & subtracting. We need to know how these operations (addition & subtraction) are done with:
  Integers in two’s complement format
  Integers in sign-and-magnitude format
  Reals in floating-point format

## Slide 38: Arithmetic Operations
  Integers in two’s complement format
  Addition
    Positive number  use binary number as is.
    Negative number  represent in 2’s complement format.
 Carry |  |  |  |  |  |  |  |  | 
(6) | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 
(9) | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | +
(15) | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 
 Carry |  |  | 1 | 1 |  |  |  |  | 
(6) | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 
(9-) | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | +
(-3) | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 
 Carry |  | 1 |  |  |  |  |  |  | 
(-15) | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 
(5) | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | +
(-10) | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 
Negative numbers always represented in 2’s complement format
Notes: http://www.allaboutcircuits.com/worksheets/binary-math/

## Slide 39: Arithmetic Operations
  Integers in two’s complement format
  Subtraction
    When the subtraction operation is encountered, the computer simply changes it to an addition operation, but makes two’s complement of the second number.
    (+24) – (-17) = (+41)
 Carry |  |  |  |  |  | 1 |  |  | 
(+24) | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 
(-17) | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | +
(+41) | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 
    (-35) – (+20) = (-55)
 Carry |  |  |  | 1 | 1 | 1 | 1 | 1 | 1
(-35) | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 
(+20) | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | +
(-55) | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 
▲in this process, the second number has to be in 2’s complement format no matter whether positive or negative
▲(-17) is negative: it is represented in 2’s complement format (11101111) and because it comes second in subtraction process, 2’s complement applied again.

## Slide 40: Arithmetic Operations
Integers in sign-and-magnitude format
  As discussed in Ch3, signed format uses the leftmost bit to represent the sign; 0 = + / 1 = -
    The leftmost bit has to remain unchanged/ not included in the adding/subtracting processes.
    The sign bit (leftmost position) must be examined first for both numbers (in process of +/-) using XOR. based on the result, 4 cases need to be considered for adding/subtracting numbers in sign-and-magnitude format.
Notes: http://www.electronics-tutorials.ws/binary/signed-binary-numbers.html

## Slide 41: Arithmetic Operations
Integers in sign-and-magnitude format
  UML Process of Addition &
  subtraction of integers in
  sign-and-magnitude format
  Showing 4 cases
Notes: http://www.electronics-tutorials.ws/binary/signed-binary-numbers.html

## Slide 42: Arithmetic Operations
Example 1:
A + B = R
(+17)10 + (-22)10 = (-5)
(0 0010001)2 +(1 0010110)2 = (1 0000101)2
Integers in sign-and-magnitude format
    Example 1
1 | 0 | 0 | 0 | 1 | 0 | 0 |  | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | + | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 |  | 
1 | 0 | 1 | 0 | 0 | 0 | 0 |  | 1
No overflow
 Carry
Notes: http://www.electronics-tutorials.ws/binary/signed-binary-numbers.html

## Slide 43: Arithmetic Operations
Example 2:
A - B = R
(-81)10 - (-22)10 = (-59)
(1 1010001)2 -(1 0010110)2 = (1 0111011)2
Integers in sign-and-magnitude format
    Example 2
 |  |  |  |  |  |  | 1 |  | 
1 | 0 | 0 | 0 | 1 | 0 | 1 |  | 1 | 
0 | 1 | 0 | 1 | 0 | 1 | 1 | + | 1 | 
1 | 1 | 0 | 1 | 1 | 1 | 0 |  | 1 | 
Overflow
 Carry
Notes: http://www.electronics-tutorials.ws/binary/signed-binary-numbers.html

## Slide 44: Arithmetic Operations
Example 3:
A + B = R
(-1)10 + (-2)10 = (-3)
(1 0000001)2 +(1 0000010)2 = (1 0000011)2
Integers in sign-and-magnitude format
    Example 3
1 | 0 | 0 | 0 | 0 | 0 | 0 |  | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | + | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 |  | 1
No overflow
 Carry
Notes: http://www.electronics-tutorials.ws/binary/signed-binary-numbers.html

## Slide 45: Arithmetic Operations
  Reals in floating-point format
  Addition and subtraction of real numbers stored in floating-point numbers is reduced to addition and subtraction of two integers stored in sign-and-magnitude (combination of sign and mantissa) after the alignment of decimal points. Figure in the next page shows a simplified version of the procedure (there are some special cases that we have ignored).

## Slide 46
Addition and subtraction of reals in floating-point format

## Slide 47: Arithmetic Operations

## Slide 48: Arithmetic Operations
  Addition & subtraction of reals in floating-point format
    Now, we treat the combination of the sign and mantissa of each number as an integer in sign-and-magnitude format. We add these two integers, as explained earlier.
    Finally, we normalized the number again.
  Example1: Show how computer finds the result of
  5.75 + 161.875 = 167.625
  Example2: Show how computer finds the result of
  5.75 + (−7.0234375) = − 1.2734375

## Slide 49: Arithmetic Operations
  Addition & subtraction of reals in floating-point format
    Example1: 5.75 + 161.875 = 167.625
    As we saw in Chapter 3, these two numbers are stored in floating-point format, as shown below, but we need to remember that each number has a hidden 1 (which is not stored, but assumed).

## Slide 50: Arithmetic Operations
  Addition & subtraction of reals in floating-point format
    Example1: 5.75 + 161.875 = 167.625
    We de-normalize the numbers by adding the hidden 1s to the mantissa and incrementing the exponent. Now both de-normalized mantissas are 24 bits and include the hidden 1s. They should be stored in a location that can hold all 24 bits. Each exponent is incremented.

## Slide 51: Arithmetic Operations
  Addition & subtraction of reals in floating-point format
    Now we do sign-and-magnitude addition, treating the sign and the mantissa of each number as one integer stored in sign-and-magnitude representation.
    There is no overflow in the mantissa, so we normalize.
    The mantissa is only 23 bits, no rounding is needed. E = (10000110)2 = 134 M = 0100111101. In other words, the result is (1.0100111101)2 × 2134−127 = (10100111.101)2 = 167.625.

## Slide 52: Arithmetic Operations
  Addition & subtraction of reals in floating-point format
  Example2: 5.75 + (−7.0234375) = − 1.2734375
    These two numbers can be stored in floating-point format, as shown below:
    De-normalization results in:

## Slide 53: Arithmetic Operations
  Addition & subtraction of reals in floating-point format
  Example2: 5.75 + (−7.0234375) = − 1.2734375
    Alignment is not needed (both exponents are the same), so we apply addition operation on the combinations of sign and mantissa. The result is shown below, in which the sign of the result is negative:
    Now we need to normalize. We decrement the exponent three times and shift the de-normalized mantissa to the left three positions:

## Slide 54: Arithmetic Operations
  Addition & subtraction of reals in floating-point format
  Example2: 5.75 + (−7.0234375) = − 1.2734375
    The mantissa is now 24 bits, so we round it to 23 bits.
    The result is R = − 2127−127 × 1.0100011 = − 1.2734375, as expected.

## Slide 55: The End 

## Slide 56: References
  Csd.uwo.ca. Available at: http://www.csd.uwo.ca/faculty/lila/logic/logicgates.pdf
  Technologystudent.com. Digital Logic Circuit Question - 3. Available at: http://www.technologystudent.com/elec1/digq3.htm
  Technologystudent.com. Digital Electronics and Logic Circuits (Role of Transistors). Available at: http://www.technologystudent.com/elec1/dig2.htm
  Technologystudent.com. Example Logic Circuit - 1. Available at: http://www.technologystudent.com/elec1/dig5.htm
  Technologystudent.com. Example Logic Circuit - 2. Available at: http://www.technologystudent.com/elec1/dig6.htm
  En.wikipedia.org. Logic gate. Available at: https://en.wikipedia.org/wiki/Logic_gate
  Bitbyte.space. Bitwise operations | Informatics. Available at: http://bitbyte.space/textbook/bitwise-operations

## Slide 57: References
  Spmphysics.onlinetuition.com.my. Logic Gates - Combination of Logic Gate. Available at: http://spmphysics.onlinetuition.com.my/2013/07/logic-gates-combination-of-logic-gate.html
  Research.microsoft.com. Designing Computers and Digital Systems. Available at: http://research.microsoft.com/en-us/um/people/gbell/Designing_Computers_and_Digital_Systems/00000104.htm
  Forouzan, B. & Mosharraf, F. (2008), Foundations of Computer Science, Second Edition, Thomson Learning.