## Slide 1
CH (6)
Computer Networks
CPIT 201 Introduction to Computing

## Slide 2
6-1 INTRODUCTION
A network is a combination of hardware and software that sends data from one location to another.
The hardware consists of the physical equipment that carries signals from one point in the network to another.
The software consists of instructions that make the services that we expect from a network possible.

## Slide 3
Network criteria
A network must be able to meet a number of criteria. The most important of these are:
1) Performance
can be measured in many ways, including transit time and response time.
  Transit Time: the amount of time required for a message to travel from one device to another
  Response Time: The elapsed time between an enquiry and a response.
Performance depends on many factors:
- number of users
- type of transmission medium - capabilities of the connected hardware - efficiency of the software

## Slide 4
Network criteria
2) Reliability
It is measured by the
  Frequency of failure
  The time it takes to recover from a failure
  The network’s robustness in a catastrophe.
3) Security
Network security issues include:
  protecting data from unauthorized access, damage and change.
  Implementing policies and procedures for recovery from breaches and data losses.

## Slide 5
Physical structures (some network attributes)
Types of Connection:
A network consists of two or more devices connected through links.
A link is a communications pathway that transfers data from one device to another.
There are two possible types of connections:
  Point-to-point and multipoint.
Provides a dedicated link between two devices.
Entire capacity of the link is reserved for transmission
Multidrop connection. More than two devices share
a single link. The capacity of the channel is shared
either spatially or temporally.

## Slide 6
Physical topology
Refers to the way in which a network is laid out physically.
The topology of a network is the geometric representation of the relationship of all links and devices (nodes).
There are four basic topologies possible: mesh, star, bus and ring.

## Slide 7
Mesh( every device has a dedicated point-to-point link to every device).
Star (each device has a dedicated point-to-point link to a central controller (a hub).
Bus (uses multipoint link, one long cable (bus) acts as a backbone to link all devices. Nodes are connected to the bus cable by drop lines and taps (connectors)).
Ring (each device has a dedicated point-to-point connection with the two devices on either side of it. A signal is passed along the ring in one direction, until it reaches its destination. Each device incorporate a repeater. When a device receives a signal for another device, its repeater regenerate the bits and passes them along.
Physical topology

## Slide 8
Physical topology
Mesh
Advantages: guarantees that each connection can carry its own data load, eliminating traffic problems. It is also robust that if one link becomes unusable, it doesn’t incapacitate the entire network.
Disadvantages: amount of cabling, number of input/output ports required.
Ring
Advantages: easy to install and reconfigure. Fault isolation is simplified
Disadvantages: a break in the ring (a disabled station) can disable the entire network. This can be solved by using a dual ring or a switch capable of closing off the break.
Bus
Advantages: easy to install.
Disadvantages: a fault or break in the bus cable stops all transmission even between devices on the same side of the problem section.
Star
Advantages: the most common in high-speed local-area networks because of: Low cost, ease of installation and scalability.
Disadvantages: dependency of the whole topology on one single point, (hub), if the hub goes down the whole system is dead.

## Slide 9
Categories of networks
Today networks can be divided into three broad categories:
local-area networks (LANs) : covers small area
Wide-area networks (WANs) : can be a Worldwide
Metropolitan area networks (MANs): covers a small city.

## Slide 10
Categories of networks
A network category is determined by its size
LAN (Local area Networks)
Privately owned and links devices in a small office, building, or campus.
Can be as simple as 2 PCs and a printer or extends, depending on the need of the organization and types of technologies used.
designed to allow resources (HW such as printer, SW such as App program, or data) to be shared between computers.
A computer may become a server to clients and SW stored on it to be used by others.
The size of LAN may be determined by licensing restrictions on the number of software copies or number of users to access the network
An isolated LAN connecting eight computers to a hub

## Slide 11
Categories of networks
WAN (Wide Area Networks)
Provides long distance transmission of information over large geographic areas (country, continent, whole world).
Can be complex (Internet backbone) or simple (dial-up line connecting a PC to the Internet).
A point-to-point WAN is a single line connection between two devices such as a dial-up line or cable line
A backbone WAN is a complex network operated by a service provider and normally connects ISPs

## Slide 12
Categories of networks
MAN (Metropolitan Area Networks)
A network with a size between a LAN and WAN.
It covers area inside a city or a town.
It is designed for customers who need high-speed connectivity to the Internet, and has end-points spread over a city.
EX: telephone companies that provide DSL.

## Slide 13
An internet
Today, it is very rare to see a network in isolation: networks are connected to one another. When two or more networks are connected, they become an internetwork, or an internet (lowercase “i”).
An internet made of WANs, LANs, and routers
The Wans are either point-to-point ( a leased line) or a backbone operated by a network service provider. Router for routing packets travelling through the internet.

## Slide 14
The Internet
The most notable internet is the Internet, a collaboration of hundreds of thousands of interconnected networks. Private individuals, various organizations such as government agencies, schools, research facilities, corporations and libraries in more than 100 countries use the Internet.
It is difficult to give an accurate representation of the Internet, because it is continually changing.
Today, most end users who want an Internet connection use the services of Internet service providers (ISPs).

## Slide 15
An ISP is an organization with one or more servers (high capacity computers) that are connected to the Internet through high-speed links.
Individual Internet users or small companies can be connected to the servers of a local ISP by establishing a service contract and paying a fee.
There are international, national, regional and local service providers.
The Internet today runs by private companies not the government.
The Internet

## Slide 16
Hierarchical organization of the Internet

## Slide 17
6-2 TCP/IP PROTOCOL SUITE
To divide the services required to perform a task, the Internet has created a set of rules called protocols.
Protocols allow different local and wide area networks, using different technologies, to be connected together and carry a message from one point to another.
The set, or suite, of protocols that controls the Internet today is referred to as the TCP/IP protocol suite.

## Slide 18
The original TCP/IP protocol suite was defined as having four layers: host-to-network (or link), internet (network), transport and application.
However, the TCP/IP protocol suite today is normally considered as a five-layer model.
The TCP/IP protocol suite

## Slide 19
The following figure shows the layers involved when a message is sent from device A to device B. As the message travels from A to B, it may pass through many routers. Routers use only the first three layers. Each layer calls on the services of the layer immediately below it and provides services to the layer above.
The interaction between layers in the TCP/IP protocol suite
Transmission media

## Slide 20
6-3 LAYERS
This section briefly describes the function of each layer in the TCP/IP protocol suite. We show how a message travels through the different layers until it reaches the physical layer and is sent by the transmission media.

## Slide 21
Application layer
The application layer enables a user (human or software) to access the network.
It provides support for services such as electronic mail, remote file access and transfer, browsing the World Wide Web, and so on. It is the only layer seen by the most users of the Internet.
The application layer is responsible for providing services to the user.

## Slide 22
Client-server architecture
There are two architectures (designs) that allow two application programs, running on two remote computers, to communicate with each other.
In client-server, each application is made up for two separate but related programs: the client program and server program.
The server program should be running all the time. The client program can be run only when needed.
Peer-to-peer architecture
Client-server architecture

## Slide 23
The communication between a client program and a server program is called process-to-process communication, because a running program in this architecture is called a process.
The user that needs the services of the server process runs the client program (changing it to a client process) and lets the client process request the service.
When a server process is running, many client processes can request services and obtain responses.

## Slide 24
Application-layer address
When a client needs to send a request to a server, it needs the server application-layer address.
For example, to identify one particular HTTP site, the client uses a Uniform Resource Locator (URL).
The address at the application-layer is not used to send a messages, it only helps the client to find the actual address of the server computer.
The client needs the actual address of the server.
Each computer in the network has an address called a logical address or IP address.
The server application-layer address can help the client to find the IP address of the server computer.

## Slide 25
The client process should already know the address of the Domain name server (DNS).
These servers have a directory that matches domain names to IP addresses.
The client prepares and sends a message to a DNS server and asks for the actual IP address of the desired server.
After receiving the response, the client server knows the IP of the desired server.

## Slide 27
Transport layer
The transport layer is responsible for process-to-process delivery of the entire message: logical communication is created between the transport layer of the client and the server computer.
In other words, although physical communication is between two physical layers (through many possible links and routers), the two application layers consider the transport layer as the agent that takes responsibility for delivering the messages.
The transport layer is responsible for the logical delivery of a message between client and server processes.

## Slide 28
Communication at the transport layer

## Slide 29
Transport-layer addresses (port numbers)
The server computer may be running several processes at the same time, for example an FTP server process and an HTTP server process.
When the message arrives at the server, it must be directed to the correct process. We need another address for server process identification, called a port number
Servers port numbers are well-known while client port number can be temporary assigned by the computer running the client process.

## Slide 31
Transport-layer duties
Logical delivery of a message
Multiplexing and demultiplexing: collecting outgoing messages from processes and distributing incoming messages using port numbers.
Congestion control: some protocols use a buffer for each process. The messages are stored in the buffer before being sent. If the transport layer detects that there is congestion in the network, it slows transmission.
Flow control: Through acknowledgment, the receiver can acknowledge receipt of each, or a group of, packets to allow the sender to check that the receiver is not overwhelmed with received packets.
Error control: a message can be corrupted, lost, duplicated, or received out of order. The acknowledgement system can also provide error control. Keeping a copy of the message in a buffer until receiving acknowledgement that the packet has arrived uncorrupted and in order. If doesn’t arrive in time, or negative one arrives, packet is resent.

## Slide 32
Transport-layer protocols
1- User Datagram Protocol (UDP)
  It is the simplest of all three protocols.
  UDP does multiplexing and de-multiplexing (by adding source and destination ports to the packet).
  It also does a type of error control (by adding a checksum to the packet). The error control is a “yes or no” procedure: the receiver recalculates the checksum to see if an error has occurred during transmission. If packet corrupted, silently drops it without warning the sender to resend it.
  Adv. Simple, fast, more efficient (carries less info overhead than other protocols). Some app prefer UDP because they either do flow and error control themselves, or need fast and efficient response. Ex: DNS. Suitable for applications that need timing more than accuracy. Ex: real-time files (videos, images).
  UDP is a connectionless protocol. It does not provide a logical connection between packets belonging to a single message.

## Slide 33
2- Transmission Control Protocol (TCP)
  It is a protocol that supports all the duties of a transport layer but it is not as fast/efficient as UDP.
  TCP uses sequence numbers, acknowledgment numbers and checksums. It also uses buffers at the sender’s site.
  This combination of provisions provides multiplexing, de-multiplexing, flow control, congestion control and error control.
  TCP is a connection-oriented protocol. It provides a logical connection between the two transport layers.
  Sequence numbers maintains a connection: if a packet arrives out of order or lost, it will be resent. The transport layer at the receiver holds all packets in a message until they are received in the correct order.
  TCP not suitable for real-time transmission. If the packet is lost, TCP needs to resend it destroys the synchronization of packets.

## Slide 34
3- Stream Control Transmission Protocol (SCTP)
It is a new protocol that is designed for new services expected from the Internet, such as Internet telephony and video streaming.
This protocol combines the advantages of both UDP and TCP.
Like UDP, it is suitable for real-time transmission of audio and video, but like TCP, it provides error and flow control.

## Slide 35
The network layer
The network layer is responsible for the source-to-destination (computer-to-computer or host-to-host) delivery of a packet, possibly across multiple networks (links).
The network layer ensures that each packet gets from its point of origin to its final destination.
The network layer protocols should provide congestion control, flow control, and error control.
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 36
Network-layer addresses
The packet traveling from the client to the server and the packet returning from the server need a network-layer address.
The server address is provided by the server while the client address is known by the client computer.
The network layer uses its routing table to find the logical address of the next hop (router), which is passed to the data link layer to find the data link layer address of the next router.

## Slide 39
Routing
The network layer has a specific duty: routing.
Routing means determination of the partial or total path of a packet.
As the Internet is a collection of networks (LANs, WANs, and MANs), the delivery of a packet from its source to its destination may be a combination of several deliveries: a source-to-router delivery, several router-to-router delivery, and finally a router-to-destination delivery.
When a router receives a packet, it consults its routing table to determine the best route to reach final destination. The routing table provides the IP address of the next router. On the next router, a new decision is made.

## Slide 40
Routing at the network layer

## Slide 41
Routers use only the first three layers of the TCP/IP protocol suite.
How routers update their routing tables? Using Routing Protocols
A routing protocol sends its own messages to all routers on the Internet to update them about routes.
Routing protocols examples: RIP, OSPF, and BGP

## Slide 42
Network-layer protocols
In the TCP/IP protocol suite, the main protocol at the network layer is Internet Protocol (IP).
The current version is IPv4. IPv6 is also in use but rarely.
IPv4 is responsible for the delivery of a packet from the source computer to the destination computer.
For this purpose, every computer and router in the world is identified by a 32-bit IP address, which is presented in dotted decimal notation.

## Slide 43
The notation divides the 32-bit address into four 8-bit sections and writes each section as a decimal number between 0 and 255 with three dots separating the sections. For example, an IPv4 address
00001010 00011001 10101100 00001111
is written as
10.25.172.15
Dotted-Decimal Notation

## Slide 44
At a message’s source, the IPv4 protocol adds the source and distention IP to the packet passed from the application.
The packet is then ready for its journey.
The actual delivery is done by data-link and physical layers.
The address range of IPv4 (32 bits) can define 232 devices. A solution for address depletion is IPv6 which address made of 128 bits.
IP provides a best-effort services.
It does not guarantee that packets will arrive error-free or in the order intended by the sender or even delivered: a packet may be lost forever (unreliable).

## Slide 45
Auxiliary protocols (to compensate its deficiencies)
  Internet Control Message Protocol (ICMP) used to report a limited number of errors to the source computer. For example, if a router drops a packet because of congestion, ICMP can send a packet to the source to warn it. ICMP can also check the status of the nodes.
  Internet Group Management Protocol (IGMP) used to add multicasting (one source, many destinations) to IP, since IP is a unicast protocol (one source, one destination).
  Address Resolution Protocol (ARP) & Reverse Address Resolution Protocol (RARP)

## Slide 46
Data link layer
As we saw in the previous section, the network layer packet may pass through several routers in its journey from its source to its destination.
Carrying the packet from one node to another (where a node can be a computer or a router) is the responsibility of the data link layer.
The data link layer is responsible for node-to-node delivery of frames.

## Slide 47
Communication at the data-link layer

## Slide 48
Data-link layer addresses
Two questions that come to mind are how computer A knows the data-link layer address of router R1, or router R1 knows the data-link layer address of router R4.
A device can find the data-link address of another device either statically or dynamically.
In the static method, a device can create a table with two columns and store NW-layer link-layer addresses pairs.
In the dynamic method, a device broadcast a packet containing the IP address of the next device and ask the neighbor with this IP to send back its link address.
Addresses at the data link layer

## Slide 49
Unlike IP addresses, addresses at the data-link layer cannot be universal.
Each data link protocol may have a different address format and size.
The Ethernet protocol, the most prevalent local area network in use today, uses a 48-bit address, which is normally written in hexadecimal format (grouped in six sections, each with two hexadecimal digits) as shown below:
Data-link layer addresses are often called physical addresses or media access control (MAC) addresses
Some data link layer protocols use error control and flow control.

## Slide 50
Physical layer
The physical layer coordinates the functions required to carry a bit stream over a physical medium.
Although the data link layer is responsible for moving a frame from one node to another, the physical layer is responsible for moving the individual bits that make up the frame to the next node.
In other words, the unit of transfer in the data link layer is a frame, while the unit of transfer in the physical layer is
a bit.
The physical layer is responsible for
node-to-node delivery of bits

## Slide 51
Duty of the physical layer
Each bit in the frame is transformed to an electromagnetic signal and propagated through the physical medium (wireless or cable).
No need for addressing in the physical layer: the propagation is broadcast.
The signal sent from a device is received by other devices that are connected to the sending device.

## Slide 52
Summary of layers
Four levels of addressing in the Internet

## Slide 53
An exchange using the TCP/IP model
Encapsulation Aspect

## Slide 54
Application Layer (5)
Physical Layer (1)
PC
M
+ d5
DNS
d5
d3
M
+ d3
M
+ d3
d4
s4
Transport Layer (4)
Network Layer (3)
Data Link Layer (2)
d3
n3
Routing Table
M
+ n3
d4
s4
d3
s3
M
d4
s4
d3
s3
d2
s2
01010101011110100000010
n3
d2
Static/
dynamic process

## Slide 55
Application Layer (5)
Provides services for the user
Transport Layer (4)
Provides logical delivery of the message between client and server process.
Network Layer (3)
Provides delivery of individual packets from the source host to the destination host.
Data Link Layer (2)
Responsible for node-to-node delivery of frames
Physical Layer (1)
Responsible for node-to-node delivery of bits
TCP/IP Layers
Protocols
HTTP FTP SMTP
UDP TCP SCTP
IP
Ethernet
-
Address
Application layer address (d5)
Port Number (d4)
IP Address (d3)
Physical address or MAC address (d2)
-
Data
Type
Message
Datagram
(Packet)
Datagram
(Packet)
Frame
Bits

## Slide 56
6-4 INTERNET APPLICATION
The main task of the Internet is to provide services for users. Among the most popular applications are electronic mail, remote login, file transfer and accessing the World Wide Web (WWW). We briefly discuss these applications in this section.

## Slide 57
Electronic-mail (e-mail)
This application cannot be supported by one client process and one server process.
The reason is that e-mail is exchange of messages between two entities.
Although the sender of the e-mail can be a client program, the receiver cannot be the corresponding server, because that implies that the receiver must let their computer run all the time, as they do not know when an e-mail will arrive.

## Slide 58
E-mail architecture
SMTP
Push & Pull
Upload & Download
POP3
IMAP
MTA client program is a push program (upload).
MAA client program is a pull program (download)

## Slide 59
Mail access protocols
Stored e-mail remains on the mail server until it is retrieved by the recipient through an access protocol.
Currently two e-mail access protocols are in common use:
  Post Office Protocol, Version 3 (POP3)
  Simple, but limited in functionality.
  The client POP software is installed on the recipient’s computer/the server POP software is installed on the email server.
  Mail access starts with the client when the user needs to download their received emails from mailbox on the email server.
  The client (user agent) sends the user name and password to access the mailbox.
  The user can then list and retrieve the email message one by one.
  POP has several deficiencies.

## Slide 60
  Internet Mail Access Protocol (IMAP)
  It is similar to POP, but it Can handle the POP deficiencies.
  Has more features and is more powerful and complex.
  Provide the following extra function
    Check an e-mail header prior to downloading.
    Search the content of their email prior to downloading.
    Partially download email.
    Create, delete, or rename mailboxes on the email server.
    Create a hierarchy of mailboxes in a folder for email storage.

## Slide 61
Addresses
Any email system should have a unique addressing system to deliver mail.
The addressing system used by SMTP consists of two parts: local part and domain part, separated by @ sign.
The local part defines the name of a special file. The user’s mailbox.
The second part is a name assigned to an IP address. The name assigned to each mail server, the domain name comes from DNS.
Each domain has IP

## Slide 62
Multipurpose Internet Mail Extension (MIME)
SMTP is a simple protocol. It can send message only in Network Virtual Terminal (NVT) 7-bit ASCII format.
MIME is a supplementary protocol that allows non-ASCII data to be sent through SMTP.
MIME is not an e-mail protocol and cannot replace SMTP, it is only an extension to SMTP.

## Slide 63
File Transfer Protocol (FTP)
The standard mechanism for one of most common tasks on the Internet, copying a file from one computer to another.
Two systems may use different file naming convention, directory structures, or text and data representation. All solved by FTP
FTP establishes two connections between the hosts. One for data transfer, and the other for control information (Commands & Responses). This separation makes FTP more efficient.
The control connection uses simple rules of communication (aline of command or response at a time) while the data connection use more complex rules due to variety of data types transferred.
Control connection remains open during FTP session, while data connection is opened and
then closed.

## Slide 64
Closed and open FTP
Two FTP strategies: Close and Open.
A closed FTP site allows only specific users to access files (usinf user accounts and passwords.
An open FTP site allows anyone to access files. User participation is very limited. For example: most sites allow users to copy files but no navigation through the file system.
When we need to copy a file without the need for other functionalities of FTP, Trivial file transfer protocol (TFTP) is designed for that.
File Transfer Protocol (FTP)

## Slide 65
Remote login – TELNET (terminal network)
The main task of the application layer is to provide services for users.
One way to satisfy these demands is to create different client-server application programs for each desired service.
Programs such as file transfer programs (FTP and SMTP), and so on are already available. However, it would be impossible to write a client-server program for each specific application.
TELNET is a general-purpose client-server program that lets a user access any application program on a remote computer.
It allows the user to log onto a remote computer. After logging on, a user can use the services available on the remote computer and transfer the results back to the local computer.
TELNET enables the establishment of a connection to a remote system.

## Slide 66
  Local Login
  When a user login onto a local time-sharing system, it is called local login.
  As the user types at a terminal or a workstation running a terminal emulator, the key-strokes are accepted by the terminal driver.
  The terminal driver passes the characters to the operating system.
  The operating system interprets the combination of characters and invokes the desired application program or utility.

## Slide 67
  Remote Login
  The operating system may assign special meaning to special characters.
  These situations don’t create any problems in local login because the terminal emulator and the terminal driver know the exact meaning of each character or combination. They may create problems in remote login

## Slide 68
The World Wide Web (WWW) “The Web”
It is a repository of linked information spread all over the world.
The WWW has a unique combination of flexibility, portability and user-friendly features that distinguish it from other services provided by the Internet.
The WWW today is a distributed client-server service in which a client using a browser can access a service using a server.
the service provided is distributed over many locations, called web sites.

## Slide 69
Hypertext and hypermedia
In a hypertext environment, information is stored in a set of documents that are connected together using the concept of links.
An item can be associated with another document using a link.
Hypertext documents contain only text, hypermedia documents can contain pictures, graphics, and sound. A unit of hypertext or hypermedia is called a page. The root page for an org is a home page.
Hypertext

## Slide 70
Components of WWW
To use the WWW we need three components:
Browser
  Commercial browsers interpret and display a web document (all browsers use nearly the same architecture).
  Consist of three parts: Controller, Client programs, and Interpreters.

## Slide 71
Web server
Stores all pages belonging to a web site.
Hypertext Transfer Protocol (HTTP)
It is a protocol used mainly to access data on the World Wide Web.
The protocol transfer data in a form of text, hypertext, audio, video,…etc.
Called HTTP because its efficiency allows its use in a hypertext environment and enables rapid jumps from one document to another.
A client sends a request, which looks like email, to the server. The server sends the response, which looks like an email reply to the client.
The request and response messages carry data in the form of a letter with a MIME-like format.

## Slide 72
A client that wants to access a document needs an address.
To facilitate the access of documents distributed throughout the world, HTTP uses the concept of locators.
The uniform resource locator (URL) is a standard for specifying any kind of information on the Internet.
URL defines four things:
  Method the protocol used to retrieve document.
  Host the computer on which the information located
  Port port number of the server (optional)
  Path the pathname of the file where the information is located.
Addresses

## Slide 73
Static documents
The documents on the WWW can be grouped into three broad categories: static, dynamic and active.
This categorization is based on the time at which the contents of the document are determined.
Static documents are fixed-content documents that are created and stored on a server.
The client can only get a copy of the documents displayed by the browser. In other words, the contents of the file are determined when the file is created, not when it is used.
The content of the server can be changed, but the user cannot change them.

## Slide 74
Hypertext Markup Language (HTML) is a language for creating Web pages.
HTML example

## Slide 75
HTML adds formatting capability to a document, but it does not define the type of data.
(XML) is a language in which tags can be used to define the content (type) of the text between two tags.
Defining the type of data in a web page makes searching easier.
The search engine could limit the search only to lines tagged with <course> to search for Universities offering CS courses.
XML documents is therefore faster to search than HTML.
Comparing HTML and XML
Pre-defined tags
User-defined tags
Extensible Markup Language(XML)

## Slide 76
Dynamic documents
A dynamic document is created by a Web server whenever a browser requests the document.
When a request arrives, the Web server runs an application program that creates the dynamic document.
The server returns the output of the program as a response to the browser that requested the document.
Contents of the document vary from one request to another.
A very simple example of a dynamic document is the retrieval of the time and date from a server.
Common Gateway Interface (CGI) is a technology that creates and handles dynamic documents. It consists of a set of standards defines how a dynamic document is written, how
data is input to the program, and how the output result is used.
It allows programmers to use any of several languages such as: C, C++, C shell, etc…

## Slide 77
Scripting technologies for dynamic documents
The problem with CGI is the inefficiency that results if part of the dynamic document that is to be created is fixed and does not change from request to request (Car Spire).
The solution is to create a file containing the fixed part of the document using HTML and embed a script, a type of source code, that can run by the server to provide the varying availability and price data.
Hypertext Preprocessor (PHP), Java Server Pages (JSP), Active Server Pages (ASP)

## Slide 78
Active documents
For many applications we need to be able to run a program or a script at the client site. These are called active documents.
For example, suppose we want to run a program that creates animated graphics on the screen, or a program that interacts with the user.
The program definitely needs to be run on the client computer where the animation or interaction takes place.
When a browser requests an active document, the server sends a copy of the document or a script.
The document is then run under the control of the client’s browser.

## Slide 79
Java Applet
One way to create an active document is to use Java Applet.
Java is a combination of a high-level programming language, a runtime environment, and a class library that allows a programmer to write an active document (applet) and a browser to run it.
An applet is a program written in Java and saved on the server, compiled and ready to be run.
The document is in byte-code (binary) format.
The client process (browser) creates an instance of this applet and runs it.
A Java applet can be run by the browser in two ways:
  Browser directly request the Java applet program in the URL and receive the applet in binary form.
  Browser retrieve and run HTML file that has embedded the address of the applet as a tag.

## Slide 80
Java Script
The idea of scripts in dynamic documents can also be used for active documents.
If the active part of the document is small, it can be written in a scripting language, which is then interpreted and run by the client.
The script is in source code (text) and not binary form.
The scripting technology used in this case is usually JavaScript.

## Slide 81
Other Internet applications
During the last decade other applications have been developed on the Internet. These applications are not as popular as those discussed above, but they are gaining ground. We discuss a few of them here.

## Slide 82
Video-conferencing
Videoconferencing can eliminate the cost of traveling, and save time and energy, by providing communication between two or more groups of participants or a set of individual participants.
Each participant uses a videoconferencing client program. The video and audio data is sent from the clients to the videoconferencing server program,then redistributes to all clients.

## Slide 83
Group discussion Listservs
Another popular class of applications is listservs, which allow a group of users to discuss a common topic of interest, EX: discussion group.
It’s a client server app. Two server programs running on the server. The subscriber server accepts membership to a group. A user sends an email addressed to this server. The user then is registered if he have permission . The subscriber server informs the user of the registration via return email.
After subscription, a user sending an email to the group, sends it to the mailer server. The mailer server automatically relays it to every member.
To unsubscribe, send a subscribe command to the subscriber server.

## Slide 84
Chat
Another popular class of Internet application is chat.
This is a real-time application like videoconferencing, in which two or more parties are involved in an exchange of text and optionally audio and video.
The two parties can send text to each other, talk to each other (the same way as they might talk on the phone), and even see each other with suitable cameras.
It works like video conferencing but on a smaller scale. The two parties each use a client program to send text, audio, or video information to a server. The server receives the information and relays the data with delay