## Slide 1: Numbering Systems
CPIT 201

## Slide 2: Non-positional Numbers
Non-positional numbers have no value impact on a symbol position.
  e.g. roman numbers

## Slide 3: Positional Numbers (1)
The position of a symbol occupies in the number determines its value.

## Slide 4: Positional Numbers (2)
Decimal System
Binary System
Octal System
Hexadecimal System

## Slide 5: Positional Numbers (3)
Decimal System
  This is what we use in our daily lives
Binary System
  This is what computer understands
Octal System
Hexadecimal System
  These two systems give easy & short ways representing blocks of binary digits.

## Slide 7: Conversions _ To Decimal (1)
Converting from any base (system) to decimal system is easy and fast
  Multiply each digit with its place/position value in the source system (i.e. binary/octal/hexa) and add the results to get the number in the destination system (i.e. decimal)

## Slide 8: Conversions _ To Decimal (2)
10
10

## Slide 9: Conversions _ To Decimal (3)
With fractional parts of the number, the positions values are negative.
  1 0 1 . 1 0 1 )2
  4 1 3 . 2 7 5 )8
  8 F C . 5 A 9 )16

## Slide 10: Conversions _ To Decimal (3)
With fractional parts of the number, the positions values are negative.
  1 0 1 . 1 0 1 )2
1 x = 0.125
0 x = 0
1 x = 0.5
1 x 1 = 1
0 x 2 = 0
1 x 4 = 4
5.625)
10

## Slide 11: Conversions _ To Decimal (3)
With fractional parts of the number, the positions values are negative.
  4 1 3 . 2 7 5 )8
5 x = 0.009
7 x = 0.11
2 x = 0.25
3 x 1 = 3
1 x 8 = 8
4 x 64 = 256
276.36)
10

## Slide 12: Conversions _ From Decimal (1)
The integral part (of the number) can be converted using repetitive divisions. It is divided by the base of the numbering system we want to convert to. If the source number (i.e. decimal) is divisible by the destination base number; then the number left over is ‘0’, otherwise we draw out from the source number until it is divisible. The drawn out number is left over.
32)10
100000)2
Number left over/remainder

## Slide 13: Conversions _ From Decimal (2)
569)10
1071)8
455)10
1C7)16

## Slide 14: Conversions _ From Decimal (3)
The fractional part (of the number) can be converted using repetitive multiplications.
  Create empty destination.
  Repeatedly multiply the source to get the result.
  The integral part of the result is inserted to the right of the destination; while the fractional part becomes the new source.
  Continue the process until reaching integral number.

## Slide 15: Conversions _ From Decimal (4)

## Slide 16: Conversions _ Binary & Octal

## Slide 17: Conversions _ Binary & Hexadecimal

## Slide 18: Conversions _ Octal & Hexadecimal