## Slide 1: William Stallings Computer Organization and Architecture 7th Edition
Chapter 3
System Buses
CPIT 210
Notes: <number>

## Slide 2: Learning Objectives
After studying this chapter, you should be able to:
  Understand the basic elements of an instruction cycle and the role of interrupts.
  Describe the concept of interconnection within a computer system.

## Slide 3: Program Concept
Modern computer is constructed based on John Von Neumann principles:
  Data and instructions are stored in a single read/Write Memory.
  The content of this memory is addressable by location without regards to the contents.
  Execution occurs in sequential fashion
Notes: <number>

## Slide 4: Hardwired systems
The computer has small set of arithmetic and logical components that can be combined (configured) in different ways (hardware programming) to store the data or to perform arithmetic and logical operations.
To perform task (sequence of operations), we need to rewire these component to achieve the task.
Hardwired systems are inflexible

## Slide 5: General purpose hardware
General purpose configuration of arithmetic and logical functions will perform the different operations according to the control signals we applied to this hardware.
By this Architecture, the system will accept data and control signals to produce result.
General purpose hardware can do different tasks, according to given correct control signals

## Slide 6: General purpose hardware & Control unit
Instead of re-wiring, we need to supply a new set of control signals.
New hardware component is needed, that is to receive the code of the different commands and generate sequence of control signals in accordance.
This new hardware unit is called control unit.

## Slide 7: Hardware and Software Approaches
Notes: In the
original case of customized hardware, the system accepts data and produces results
(Figure 3.1a). With general-purpose hardware, the system accepts data and control
signals and produces results. Thus, instead of rewiring the hardware for each new
program, the programmer merely needs to supply a new set of control signals.
and let us add to the general-purpose hardware a segment that can accept a code
and generate control signals (Figure 3.1b).
Figure 3.1b indicates two major components of the system: an instruction
interpreter and a module of general-purpose arithmetic and logic functions. These
two constitute the CPU. Several other components are needed to yield a functioning
computer. Data and instructions must be put into the system. For this we need
some sort of input module. This module contains basic components for accepting
data and instructions in some form and converting them into an internal form
of signals usable by the system. A means of reporting results is needed, and this
is in the form of an output module. Taken together, these are referred to as I/O
components.
One more component is needed. An input device will bring instructions and
data in sequentially. But a program is not invariably executed sequentially; it may
jump around (e.g., the IAS jump instruction). Similarly, operations on data may
require access to more than just one element at a time in a predetermined sequence.
Thus, there must be a place to temporarily store both instructions and data. That
module is called memory, or main memory, to distinguish it from external storage or
peripheral devices. Von Neumann pointed out that the same memory could be used
to store both instructions and data.
<number>

## Slide 8: What is a program?
A sequence of steps
For each step, an arithmetic or logical operation is done
For each operation, a different set of control signals is needed
The program interpreted by control unit as sequence of control signals is called the software
Notes: <number>

## Slide 9: Function of Control Unit
For each operation a unique code is provided
  e.g. ADD, MOVE
A hardware segment accepts the code and issues the control signals
We have a computer!
Notes: <number>

## Slide 10: Components
The Control Unit and the Arithmetic and Logic Unit constitute the Central Processing Unit
Data and instructions need to get into the system and results out
  Input/output
Temporary storage of code and results is needed
  Main memory
Notes: <number>

## Slide 11: Computer Components: Top Level View
Notes: <number>
Figure 3.2 illustrates these top-level components and suggests the interactions
among them.
The CPU exchanges data with memory. For this purpose, it typically
makes use of two internal (to the CPU) registers: a memory address register
(MAR), which specifies the address in memory for the next read or write, and a
memory buffer register (MBR), which contains the data to be written into memory
or receives the data read from memory. Similarly, an I/O address register (I/OAR)
specifies a particular I/O device. An I/O buffer register (I/OBR) is used for the
exchange of data between an I/O module and the CPU.
A memory module consists of a set of locations, defined by sequentially numbered
addresses. Each location contains a binary number that can be interpreted as
either an instruction or data. An I/O module transfers data from external devices to
CPU and memory, and vice versa. It contains internal buffers for temporarily holding
these data until they can be sent on.

## Slide 12: Instruction Cycle
Two steps:
  Fetch & Decode
  Execute
Notes: <number>
The processing required for a single instruction is called an instruction cycle.
Using the simplified two-step description given previously, the instruction cycle is
depicted in Figure 3.3. The two steps are referred to as the fetch cycle and the execute
cycle. Program execution halts only if the machine is turned off, some sort of unrecoverable
error occurs, or a program instruction that halts the computer is encountered.

## Slide 13: Fetch & Decode Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor decodes (interprets) instruction and performs required actions
Notes: <number>

## Slide 14: Instruction Action Categories
Processor-memory
  Data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above can be held by single instruction
Notes: <number>
The fetched instruction is loaded into a register in the processor known as
the instruction register (IR). The instruction contains bits that specify the action
the processor is to take. The processor interprets the instruction and performs the
required action. In general, these actions fall into four categories:
■■ Processor-memory: Data may be transferred from processor to memory or
from memory to processor.
■■ Processor-I/O: Data may be transferred to or from a peripheral device by
transferring between the processor and an I/O module.
■■ Data processing: The processor may perform some arithmetic or logic operation
on data.
■■ Control: An instruction may specify that the sequence of execution be altered.
For example, the processor may fetch an instruction from location 149, which
specifies that the next instruction be from location 182. The processor will
remember this fact by setting the program counter to 182. Thus, on the next
fetch cycle, the instruction will be fetched from location 182 rather than 150.

## Slide 15: Instructions and Data Format
As simple example, consider hypothetical machine that holds data and instructions in a words of 16 bit length (2 bytes).
4 bits are used to hold the operation code (Opcode), allows up to 16 different operations 24.
Numbers are represented sign-magnitude format
Opcode
Address/Operand
0
15
4
3

## Slide 16: Instructions and Data Format
Internal CPU Registers:
  Program Counter(PC)= address of instruction
  Instruction Register(IR)= Instruction being executed
  Accumulator(AC)= Temporary Storage
Partial List of opcodes:
  0001 = Load AC from memory
  0010 = Store AC to memory
  0101 = Add AC from memory

## Slide 17: Example of Program Execution
Notes: <number>

## Slide 18: Example of Program Execution
 | PC | IR | AC | Memory
Instruction1 (Fetch & Decode) | 300 | 1940 (1) Load instruction | ----- | 0003 in address 940
Instruction1 (Execute) | 301 | 1940 | 0003 (load AC with data stored in 940) | 
Instruction2 (Fetch & Decode) | 301 | 5941 (5) Add Instruction | 0003 | 0002 in address 941
Instruction2 (Execute) | 302 | 5941 | 0003+0002= 0005 | 
Instruction3 (Fetch & Decode) | 302 | 2941 (2) Store Instruction | 0005 | -----
Instruction3 (Execute) | 303 | 2941 | 0005 | Store AC in Location 941

## Slide 19: Example of Program Execution
The PC contains 300, the address of the first instruction.
1940 in hexadecimal is loaded into the instruction register IR, and the PC is incremented.
The first 4 bits in the IR indicate that the AC is to be
loaded. The remaining 12 bits specify the address (940) from which data are to be loaded.
3. The next instruction (5941) is fetched from location 301, and the PC is incremented.
4. The old contents of the AC and the contents of location 941 are added, and the result is stored in the AC.
5. The next instruction (2941) is fetched from location 302, and the PC is incremented.
6. The contents of the AC are stored in location 941.
Notes: Note that this process involves the use of a memory
address register and a memory buffer register. For simplicity, these intermediate
registers are ignored.
For example, the PDP-11 processor includes an instruction, expressed symbolically
as ADD B,A, that stores the sum of the contents of memory locations B and A
into memory location A. A single instruction cycle with the following steps occurs:
■■ Fetch the ADD instruction.
■■ Read the contents of memory location A into the processor.
■■ Read the contents of memory location B into the processor. In order that the
contents of A are not lost, the processor must have at least two registers for
storing memory values, rather than a single accumulator.
■■ Add the two values.
■■ Write the result from the processor to memory location A.
<number>

## Slide 20: Instruction Cycle State Diagram
Notes: <number>
The figure is in the form
of a state diagram. For any given instruction cycle, some states may be null and others
may be visited more than once. The states can be described as follows:
■■ Instruction address calculation (iac): Determine the address of the next
instruction to be executed. Usually, this involves adding a fixed number to
States in the upper part of Figure 3.6 involve an exchange between the processor
and either memory or an I/O module. States in the lower part of the diagram
involve only internal processor operations. The oac state appears twice, because
an instruction may involve a read, a write, or both. However, the action performed
during that state is fundamentally the same in both cases, and so only a single state
identifier is needed.
Also note that the diagram allows for multiple operands and multiple results,
because some instructions on some machines require this.

## Slide 21: Instruction Cycle State Diagram
The figure is in the form of a state diagram. For any given instruction cycle, the states can be described as follows:
  Instruction address calculation (iac): Determine the address of the next instruction to be executed.
  Instruction fetch (if): Read instruction from its memory location into the processor.
  Instruction operation decoding (iod): Analyze instruction to determine type of operation to be performed and operand(s) to be used.
  Operand address calculation (oac): If the operation involves reference to an operand in memory or available via I/O, then determine the address of the operand.
  Operand fetch (of): Fetch the operand from memory or read it in from I/O.
  Data operation (do): Perform the operation indicated in the instruction.
  Operand store (os): Write the result into memory or out to I/O.
Notes: <number>

## Slide 22: Interrupts
Virtually all computers provide a mechanism by which other modules (I/O, memory)
Interrupts are provided primarily as a way to improve processing efficiency.
For example:
  Most external devices are much slower than the processor.
  Suppose that the processor is transferring data to a printer using the instruction cycle scheme
  After each write operation, the processor must pause and remain idle until the printer catches up.
  The length of this pause may be on the order of many hundreds or even thousands of instruction cycles that do not involve memory.
  Clearly, this is a very wasteful use of the processor.
Notes: Interrupt the normal processing of the processor.
<number>

## Slide 23: Class of Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error
Notes: <number>

## Slide 24: Program Flow Control
Notes: <number>

## Slide 25: Program Flow Control

## Slide 26: Program Flow Control
We have a user program that contains two WRITE commands.
There is a segment of code at the beginning, then one WRITE command, then a second segment of code, then a second WRITE command, then a third and final segment of code.
The WRITE command invokes the I/O program provided by the OS.
Similarly, the I/O program consists of a segment of code, followed by an I/O command, followed by another segment of code.
The I/O command invokes a hardware I/O operation.

## Slide 27: Program Flow Control(No Interrupts)
User Program:
  Performs a series of WRITE calls interleaved with processing.
  Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O.
  The WRITE calls are to an I/O program that is a system utility and that will perform the actual I/O operation.

## Slide 28: Program Flow Control(No Interrupts)
The I/O program consists of three sections:
  A sequence of instructions, labeled 4 in the figure, to prepare for the actual I/O operation.
  The actual I/O command. Without the use of interrupts, once this command is issued, the program must wait for the I/O device to perform the requested function.
  A sequence of instructions, labeled 5 in the figure, to complete the operation.
  This may include setting a flag indicating the success or failure of the operation.
Notes: I/O operation. This may include copying the data to be output into a special buffer and preparing the parameters for a device command.
The program might wait by simply repeatedly performing a test operation to determine if the I/O operation is done.
Because the I/O operation may take a relatively long time to complete, the I/O
program is hung up waiting for the operation to complete; hence, the user program
is stopped at the point of the WRITE call for some considerable period of time.
<number>

## Slide 29: Program Flow Control(with Interrupts)
Consider the flow of control in Figure b:
  The user program reaches a point at which it makes a system call in the form of a WRITE call.
  The I/O program consists only of the preparation code and the actual I/O command.
  After these few instructions have been executed, control returns to the user program.
  Meanwhile, the external device is busy accepting data from computer memory and printing it.
  This I/O operation is conducted concurrently with the execution of instructions in the user program.
Notes: When the external device becomes ready to be serviced—that is, when it is ready to accept more data from the processor—the I/O module for that external device sends an interrupt request signal to the processor. The processor responds by suspending operation of the current program, branching off to a program to service that particular I/O device, known as an interrupt handler, and resuming the original execution after the device is serviced.
<number>

## Slide 30: Interrupt Cycle
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program
Notes: <number>

## Slide 31: Transfer of Control via Interrupts

## Slide 32: Instruction Cycle with Interrupts
Notes: To accommodate interrupts, an interrupt cycle is added to the instruction
cycle, as shown in Figure 3.9. In the interrupt cycle, the processor checks to see if
any interrupts have occurred, indicated by the presence of an interrupt signal. If no
interrupts are pending, the processor proceeds to the fetch cycle and fetches the
next instruction of the current program
<number>

## Slide 33: Instruction Cycle with Interrupts
If an interrupt is pending, the processor does the following:
  It suspends execution of the current program being executed and saves its context. This means saving the address of the next instruction to be executed (current contents of the program counter) and any other data relevant to the processor’s current activity.
  It sets the program counter to the starting address of an interrupt handler routine.
  The processor now proceeds to the fetch cycle and fetches the first instruction in the interrupt handler program, which will service the interrupt.
  When the interrupt handler routine is completed, the processor can resume execution of the user program at the point of interruption.

## Slide 34: Program Timing Short I/O Wait
Notes: In this figure, user program code segments are shaded green, and I/O program code segments are shaded gray. Figure 3.10a shows the case in which interrupts are not used. The processor
must wait while an I/O operation is performed.
Figures 3.7b and 3.10b assume that the time required for the I/O operation is relatively
short: less than the time to complete the execution of instructions between write
operations in the user program. In this case, the segment of code labeled code segment 2
is interrupted. A portion of the code (2a) executes (while the I/O operation is performed)
and then the interrupt occurs (upon the completion of the I/O operation). After the interrupt
is serviced, execution resumes with the remainder of code segment 2 (2b).
The more typical case, especially for a slow device such as a printer, is that the
I/O operation will take much more time than executing a sequence of user instructions.
Figure 3.7c indicates this state of affairs. In this case, the user program reaches
the second WRITE call before the I/O operation spawned by the first call is complete.
The result is that the user program is hung up at that point. When the preceding
I/O operation is completed, this new WRITE call may be processed, and a new
I/O operation may be started. Figure 3.11 shows the timing for this situation with
<number>

## Slide 35: Program Timing Short I/O Wait
User program code segments are shaded green, and I/O program code segments are shaded gray.
Figure 3.10a shows the case in which interrupts are not used. The processor must wait while an I/O operation is performed.
Figures 3.10b assume that the time required for the I/O operation is relatively short.
  In this case, the segment of code labeled code segment 2 is interrupted.
  A portion of the code (2a) executes and then the interrupt occurs.
  After the interrupt is serviced, execution resumes with the remainder of code segment 2 (2b).
Notes: less than the time to complete the execution of instructions between write operations in the user program.
<number>

## Slide 36: Program Timing Long I/O Wait
Notes: The more typical case, especially for a slow device such as a printer, is that the
I/O operation will take much more time than executing a sequence of user instructions.
Figure 3.7c indicates this state of affairs. In this case, the user program reaches
the second WRITE call before the I/O operation spawned by the first call is complete.
The result is that the user program is hung up at that point. When the preceding
I/O operation is completed, this new WRITE call may be processed, and a new
I/O operation may be started. Figure 3.11 shows the timing for this situation with
<number>

## Slide 37: Program Timing Long I/O Wait
The more typical case, especially for a slow device such as a printer, is that the I/O operation will take much more time than executing a sequence of user instructions.
In this case, the user program reaches the second WRITE call before the I/O operation spawned by the first call is complete.
The result is that the user program is hung up at that point.
When the preceding I/O operation is completed, this new WRITE call may be processed, and a new I/O operation may be started.

## Slide 38: Instruction Cycle (with Interrupts) - State Diagram
Notes: <number>

## Slide 39: Multiple Interrupts
Disable interrupts
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt
Notes: <number>

## Slide 40: Multiple Interrupts - Sequential
Notes: <number>

## Slide 41: Multiple Interrupts – Nested
Notes: <number>

## Slide 42: Time Sequence of Multiple Interrupts
60
Priority:
1-communication
2-Disk
3-Printer
Time of call occurrence:
Printer t=10 (need 30)
Communication t=15 (need 10)
Dsk=20 (need 10)
Notes: ISR = Interrupt Service Routine
<number>

## Slide 43: Connecting
All the units must be connected.
Different type of connection for different type of unit
  Memory
    The operation is indicated by read and write control signals.
    The location for the operation is specified by an address.
  Input/Output
    There are two operations; read and write
    a port is an interface to an external device as and give each a unique address
    there are external data paths for the input and output of data with an external device address
    able to send interrupt signals to the processor
  CPU
    Reads in instructions and data, writes out data after processing
    uses control signals to control the overall operation of the system.
    It also receives interrupt signals.
Notes: <number>
    consist of N words of equal length.
    Each word is assigned a unique numerical address.
    A word of data can be read from or written into the memory.

## Slide 44: Computer Modules
■■ Memory to processor: The processor reads an instruction or a unit of data
from memory.
■■ Processor to memory: The processor writes a unit of data to memory.
■■ I/O to processor: The processor reads data from an I/O device via an I/O module.
■■ Processor to I/O: The processor sends data to the I/O device.
■■ I/O to or from memory: For these two cases, an I/O module is allowed to
exchange data directly with memory, without going through the processor,
using direct memory access (DMA).
Notes: Memory to processor: The processor reads an instruction or a unit of data
from memory.
■■ Processor to memory: The processor writes a unit of data to memory.
■■ I/O to processor: The processor reads data from an I/O device via an I/O
module.
■■ Processor to I/O: The processor sends data to the I/O device.
■■ I/O to or from memory: For these two cases, an I/O module is allowed to
exchange data directly with memory, without going through the processor,
using direct memory access.
<number>

## Slide 45: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing
Notes: <number>

## Slide 46: Input/Output Connection(1)
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer
Notes: <number>

## Slide 47: Input/Output Connection(2)
Receive control signals from computer
Send control signals to peripherals
  e.g. spin disk
Receive addresses from computer
  e.g. port number to identify peripheral
Send interrupt signals (control)
Notes: <number>

## Slide 48: CPU Connection
Reads instruction and data
Writes out data (after processing)
Sends control signals to other units
Receives (& acts on) interrupts
Notes: <number>

## Slide 49: Buses
There are a number of possible interconnection systems
Single and multiple BUS structures are most common
e.g. Control/Address/Data bus (PC)
e.g. Unibus (DEC-PDP)
Notes: <number>

## Slide 50: What is a Bus?
A communication pathway connecting two or more devices
Usually broadcast
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
Power lines may not be shown
Notes: <number>
A bus is a communication pathway connecting two or more devices.
A key characteristic of a bus is that it is a shared transmission medium.
Multiple devices connect to the bus, and a signal transmitted by any one device is available for reception
by all other devices attached to the bus.
If two devices transmit during the same time period, their signals will overlap and become garbled.
Thus, only one device at a time can successfully transmit.
an 8-bit unit of data can be transmitted over eight bus lines.

## Slide 51: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Connects major computer components (processor, memory, I/O)
Width is a key determinant of performance
  8, 16, 32, 64 bit
Notes: <number>

## Slide 52: Address bus
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space
Notes: <number>

## Slide 53: Control Bus
Control and timing information
Typical control lines include:
  Memory write: causes data on the bus to be written into the addressed location.
  Memory read: causes data from the addressed location to be placed on the bus.
  I/O write: causes data on the bus to be output to the addressed I/O port.
  I/O read: causes data from the addressed I/O port to be placed on the bus.
  Transfer ACK: indicates that data have been accepted from or placed on the bus.
  Bus request: indicates that a module needs to gain control of the bus.
  Bus grant: indicates that a requesting module has been granted control of the bus.
  Interrupt request: indicates that an interrupt is pending.
  Interrupt ACK: acknowledges that the pending interrupt has been recognized.
  Clock: is used to synchronize operations.
  Reset: initializes all modules.
Notes: <number>

## Slide 54: Bus Interconnection Scheme
Notes: <number>

## Slide 55: Bus Interconnection Scheme
The data lines provide a path for moving data among system modules.
These lines, collectively, are called the data bus.
The width of the data bus is a key factor in determining overall system performance.
The address lines are used to designate the source or destination of the data on the data bus.
The address lines are generally also used to address I/O ports.
The control lines are used to control the access to and the use of the data and address lines. Because the data and address lines are shared by all components,
Notes: For example, on an 8-bit address bus, address 01111111 and below might reference
locations in a memory module (module 0) with 128 words of memory, and address
10000000 and above refer to devices attached to an I/O module (module 1).
<number>

## Slide 56: Bus Interconnection Scheme
The operation of the bus is as follows.
  If one module wishes to send data to another, it must do two things:
  (1) obtain the use of the bus, and
  (2) transfer data via the bus.
    -If one module wishes to request data from another module, it must do three things:
  (1) obtain the use of the bus, and
  (2) transfer a request to the other module over the appropriate control and address lines.
  (3) It must then wait for that second module to send the data.

## Slide 57: Big and Yellow?
What do buses look like?
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
    e.g. PCI
  Sets of wires
Notes: <number>

## Slide 58: Physical Realization of Bus Architecture
Notes: <number>

## Slide 59: Single Bus Problems
Lots of devices on one bus leads to:
  Propagation delays
    Long data paths mean that co-ordination of bus use can adversely affect performance
    If aggregate data transfer approaches bus capacity
Most systems use multiple buses to overcome these problems
Notes: <number>

## Slide 60: Traditional (ISA) (with cache)
Notes: <number>
Traditional Bus Architecture
A local bus connects the processor to the cache memory, which may support one or more local devices. There is also a cache memory controller that connects this cache to this local bus and the system bus.
On the system, the bus is attached to the main memory modules. In this way, I/O transfers to and from the main memory across the system bus do not interfere with the processor’s activity. An expansion bus interface buffers data transfers between the bus and the I/O controllers on the expansion bus.
Some typical I/O devices that might be attached to the expansion bus include
Network cards (LAN)
SCSI (Small Computer System Interface)
Modem
Serial Com
Advantages of Traditional Bus Architecture
A separate cache structure insulates the processor from the requirement to access the main memory frequently.
This arrangement allows the system to support a wide variety of I/O devices and, at the same time, insulate memory to processor traffic from I/O traffic.
Disadvantages of Traditional Bus Architecture
The traditional bus architecture is reasonably efficient but begins to break down as higher and higher performance is seen in the I/O devices.

## Slide 61: High Performance Bus
Notes: <number>
High-Performance Bus Architecture
Similar to the previous arrangement, there is a local bus that connects the processor to a cache controller, which is, in turn, connected to a system bus that supports the main memory.
The cache controller is integrated into a bridge or buffering device that connects to a high-speed bus.
This (High Speed) bus supports connections to high-speed LANs, such as Fast Ethernet at 100 Mbps, video, and graphics workstation controllers to local peripheral busses, including SCSI and Firewire.
Lower speed devices are still supported off an expansion bus, with an interface buffering traffic between the expansion bus and the high-speed bus.
Advantages of High-Performance Bus Architecture
The advantage of this arrangement is that the high-speed bus brings high demand devices into closer integration with the processor and at the same time is independent of the processor
So changes in processor architecture also do not affect the high-speed bus.

## Slide 62: Bus Types
Dedicated
  Separate data & address lines
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Ultimate performance
Notes: <number>

## Slide 63
Notes: <number>