## Slide 1: William Stallings Computer Organization and Architecture 7th Edition
Chapter 10
Instruction Sets:
Characteristics and Functions

## Slide 2: What is an Instruction Set?
The complete collection of instructions that are understood by a CPU
Machine Code
Binary
Usually represented by assembly codes
Notes: 2

## Slide 3: Elements of an Instruction
Operation code (Op code)
  Do this
Source Operand reference
  To this
Result Operand reference
  Put the answer here
Next Instruction Reference
  When you have done that, do this...[i.e. the next instruction to fetch, often is the immediately follow the current instruction, only explicit reference is needed when need to jump else where].
Notes: 3

## Slide 4: Where have all the Operands Gone?
Main memory (or virtual memory or cache)
CPU registers
I/O device (in case of memory mapped I/O the reading the operands are fetched by the same way as the fetching the operands from memory.
Notes: 4

## Slide 5: Instruction Cycle State Diagram

## Slide 6: Instruction Representation
In machine code each instruction has a unique bit pattern divided into fields
For human consumption (well, programmers anyway) a symbolic representation is used
  e.g. ADD, SUB, LOAD
Operands can also be represented in this mnemonic way
  ADD A,B
Notes: 5

## Slide 7: Simple Instruction Format

## Slide 8: Instruction Types
Data processing (arithmetic and logic instructions)
Data storage (main memory): to transfer data to/from memory (store or fetch data and instructions)
Data movement (I/O) to transfer program and data to memory
Program flow control : to execute the decision and looping instruction.
Notes: 6

## Slide 9: Number of Addresses (a)
3 addresses
  Consists of two operands (Operand 1, Operand 2) in additional to the address of the Result
  Ex. The next instruction can be represented by single add instruction with three operands (a = b + c;)
  May be a forth (2 data operands, result operand and the next instruction operands)–next instruction address is being implicit.
  Forth instruction format not common as well as 3-instructions format
  The reason is the need for very long words to hold everything
Notes: 7

## Slide 10: Number of Addresses (a)
Y= (A-B)/[C+(D*E)]
The 3-address instruction is used in the following program to execute the above high level instruction
Sub Y, A,B
MPY T, D,E
ADD T,T, C
DIV Y, Y, T

## Slide 15: Number of Addresses (b)
2 addresses
  One address doubles as operand and result
  a = a + b (one of the operands is used as data and result)
  Reduces length of instruction
  Requires some extra work
    Temporary storage to hold some results
    MOVE Y, A
    SUB Y, B
    MOVE T,D
    MPY T,E
    ADD T, C
    DIV Y, T
Y= (A-B)/[C+(D*E)]
Notes: 8

## Slide 16: Number of Addresses (c)
1 address
  Implicit second address
  Usually a register (accumulator)
  Common on early machines
  MOVE D
  MPY E
  ADD C
  STORE Y
  MOVE A
  SUB B
  DIV Y
  STORE Y
Y= (A-B)/[C+(D*E)]
Notes: 9

## Slide 17: Number of Addresses (d)
0 (zero) addresses
  All addresses implicit
  Uses a stack
  e.g. push a
  push b
  add
  pop c
  c = a + b
Notes: 10

## Slide 18: How Many Addresses
More addresses
  More complex (powerful?) instructions
  More registers
    Inter-register operations are quicker
  Fewer instructions per program
Fewer addresses
  Less complex (powerful?) instructions
  More instructions per program
  Faster fetch/execution of instructions
Notes: 11

## Slide 19: Design Decisions (1)
Operation repertoire
  How many ops?
  What can they do?
  How complex are they?
Data types
Instruction formats
  Length of op code field
  Number of addresses
Notes: 12

## Slide 20: Design Decisions (2)
Registers
  Number of CPU registers available
  Which operations can be performed on which registers?
Addressing modes (later…)
RISC v CISC
  RISC (Reduced instruction set computing)
  CISC (Complex instruction set computing)
Notes: 13

## Slide 21: Types of Operand
Addresses
Numbers
  Integer/floating point
Characters
  ASCII etc.
Logical Data
  Bits or flags
(Aside: Is there any difference between numbers and characters? Ask a C programmer!)
Notes: 14

## Slide 22: Pentium Data Types
8 bit Byte
16 bit word
32 bit double word
64 bit quad word
Addressing is by 8 bit unit
A 32 bit double word is read at addresses divisible by 4
Notes: 15

## Slide 23: Specific Data Types
General - arbitrary binary contents
Integer - single binary value
Ordinal - unsigned integer
Unpacked BCD - One digit per byte
Packed BCD - 2 BCD digits per byte
Near Pointer - 32 bit offset within segment
Bit field
Byte String
Floating Point
Notes: 16

## Slide 24: Pentium Numeric Data Formats
Notes: 17

## Slide 25: PowerPC Data Types
8 (byte), 16 (halfword), 32 (word) and 64 (doubleword) length data types
Some instructions need operand aligned on 32 bit boundary
Can be big- or little-endian
Fixed point processor recognises:
  Unsigned byte, unsigned halfword, signed halfword, unsigned word, signed word, unsigned doubleword, byte string (<128 bytes)
Floating point
  IEEE 754
  Single or double precision

## Slide 26: Types of Operation
Data Transfer
Arithmetic
Logical
Conversion
I/O
System Control
Transfer of Control
Notes: 18

## Slide 27: Data Transfer
Specify
  Source
  Destination
  Amount of data
May be different instructions for different movements
  e.g. IBM 370
Or one instruction and different addresses
  e.g. VAX
Notes: 19

## Slide 28: Arithmetic
Add, Subtract, Multiply, Divide
Signed Integer
Floating point ?
May include
  Increment (a++)
  Decrement (a--)
  Negate (-a)
Notes: 20

## Slide 29: Shift and Rotate Operations

## Slide 30: Logical
Bitwise operations
AND, OR, NOT
Notes: 21

## Slide 31: Conversion
E.g. Binary to Decimal
Notes: 22

## Slide 32: Input/Output
May be specific instructions
May be done using data movement instructions (memory mapped)
May be done by a separate controller (DMA)
Notes: 23

## Slide 33: Systems Control
Privileged instructions
Those instructions required by to be executed in the privileged state.
CPU needs to be in specific state
  Ring 0 on 80386+
  Kernel mode
For operating systems use.
Ex. Changing the protection key of memory or accessing the process contol blocks of processes.
Notes: 24

## Slide 34: Transfer of Control
Branch (BRP X, PRN X, PRZ X, PRO X)
  e.g. BRZ X : means go to X if result is zero
Skip
  e.g. increment and skip if zero
  ISZ Register1
  Branch xxxx
  ADD A
Notes: 25

## Slide 35: Usage of Transfer Control instructions
To be able to execute set of instructions more than once.
While (x ==y){
instructions here
}
Load x
Sub y
BRZ 5
BR 8
instructions here
….
BR 1
AFTER LOOP

## Slide 36: Usage of Transfer Control instructions
To be able to make decision.
If (x  y){
instruction 1
}else {
instruction 2
}
Load X
Sub Y
BRZ 6
Instruction 1
BR 7
Instruction 2
remaining instructions

## Slide 37: Branch Instruction

## Slide 38: Usage of Transfer Control instructions
To allow breaking big program into smaller tasks through using procedure call.
Procedure is self contained program incorporated into larger program.
Reasons for using procedure:
  Economy by saving writing the same code many times.
  Modularity : since each procedure module will have specific task (different modules interact together through well defined interface).

## Slide 39: Nested Procedure Calls

## Slide 40: Use of Stack

## Slide 41: Procedure call
Can be called from any where.
Procedure call can appear in procedure (nested).
Each procedure call is matched with return in the called program.
return address
  register
  Start of the called procedure
  Top of stack (used often to allow recursion)

## Slide 42: Procedure call
Register
Call X (is used to call procedure) the action is:
  RN  PC + 
  PC  x
  RN is a register used to keep the return address and  is the length of the instruction.
At the start of called procedure:
The action is
  X  PC + 
  PC  X + 1

## Slide 43: Procedure call
  The previous two methods prevents the recursion (reentrant).
  Alternative for the above method is using stack.
  X  PC + 
  PC  X + 1
Not only the return address is passed on the stack but the parameter values as well.
Local variable is also stored on the stack with each beginning of procedure.

## Slide 44: Stack Frame Growth Using Sample Procedures P and Q

## Slide 45: Exercise For Reader
Find out about instruction set for Pentium and PowerPC
Start with Stallings
Visit web sites

## Slide 46: Byte Order (A portion of chips?)
What order do we read numbers that occupy more than one byte
e.g. (numbers in hex to make it easy to read)
12345678 can be stored in 4x8bit locations as follows
Notes: 27

## Slide 47: Byte Order (example)
Address Value (1) Value(2)
184 12 78
185 34 56
186 56 34
186 78 12
i.e. read top down or bottom up?
Notes: 28

## Slide 48: Byte Order Names
The problem is called Endian
The system on the left has the least significant byte in the lowest address
This is called big-endian
The system on the right has the least significant byte in the highest address
This is called little-endian
Notes: 29

## Slide 49: Example of C Data Structure

## Slide 50: Alternative View of Memory Map

## Slide 51: Standard…What Standard?
Pentium (80x86), VAX are little-endian
IBM 370, Moterola 680x0 (Mac), and most RISC are big-endian
Internet is big-endian
  Makes writing Internet programs on PC more awkward!
  WinSock provides htoi and itoh (Host to Internet & Internet to Host) functions to convert
Notes: 30