## Slide 1: Analog Versus Digital
Dr. M. Khamis

## Slide 2: Analog Signal
analog signal is a continuous wave vary in signal strength (amplitude) or frequency.
Example: The audio and video streams resulted from microphone or from analog camera. This analog signal takes different shapes according to its physical source.
digital signal - used for computer processing - is described as using binary (0s and 1s), and therefore, cannot take on any fractional values. As illustrated in the graphic below.

## Slide 3: Analog Signal
Each analog signal can be transformed to digital using special electronic circuit called Analog to Digital Converter (ADC)

## Slide 4: How analog transformed to digital
In analog technology, a wave is recorded or used in its original form. So, for example, in an analog tape recorder, a signal is taken straight from the microphone and laid onto tape.
In digital technology, the analog wave is sampled at some interval, and then turned into numbers that are stored in the digital device such as CD or DVD.
The red lines in the above figure is the samples corresponding to analog signal appears in continuous black line

## Slide 5: How analog transformed to digital
Sampling is process of taking samples at regular interval of time instead of sending the continues analog signal and then sending each sample values in binary form {0, 1}.

## Slide 6: How analog transformed to digital
The quality of transforming analog to digital is determined by:
  Number of quantization levels: increasing the number of levels increase the quality as the error for recording sample will decrease but also increase the levels will increase the number of bits to represent levels value (for example if we consider 256 levels: i.e. each sample will take 8 bits in binary).
  for number of levels L= 2n needs n of bits for each sample.
  The number of samples per second: with increasing the number of samples per second, the more details of analog signal is taken, but again increase the number of samples will increase the storage to record the samples.

## Slide 7: Analog versus Digital
Analog signal suffers from the follow:
  Attenuation: degrade the signal during transfer from point to other point (i.e. weaken).
  Noise : the unwanted signal merges with the wanted one and introduce some error on the original signal.
  Cross-talk : original signal with other original signal propagate on the same cable or contagious cable causes interference from each one into the other.
Digital signal
  Digital signal maintain their quality over long distance better than analog because we are always able to restore and repeat the original signal without the problems associated with the analog signal.
  The quality of the digital signal is better than that of the analog signal.

## Slide 8: Analog versus Digital
  Digital data can be easily compressed.
  Any information in the digital form can be encrypted.
  Equipment that uses digital signals is more common and less expensive.
  Easy to transmit the data over networks.
  The digital data can be processed using different algorithm to extract different information such face recognition for digital photos and voice recognition and many other information.
  End of analog and

## Slide 9: Analog versus Digital
  Digital data can be easily compressed.
  Any information in the digital form can be encrypted.
  Equipment that uses digital signals is more common and less expensive.
  Easy to transmit the data over networks.
  The digital data can be processed using different algorithm to extract different information such face recognition for digital photos and voice recognition and many other information.