## Slide 1: William Stallings Computer Organization and Architecture 7th Edition
Chapter 3
System Buses
Notes: <number>

## Slide 2: Hardwired systems
The computer has small set of arithmetic and logical components that can be combined (configured) in different ways (hardware programming) to store the data or to perform arithmetic and logical operations.
To perform task (sequence of operations), we need to rewire these component to achieve the task.
Hardwired systems are inflexible

## Slide 3: General purpose hardware
General purpose configuration of arithmetic and logical functions will perform the different operations according to the control signals we applied to this hardware.
By this Architecture, the system will accept data and control signals to produce result.
General purpose hardware can do different tasks, according to given correct control signals

## Slide 4: Program Concept
Modern computer is constructed based on John Von Neumann principles:
  Data and instructions are stored in a single read/Write Memory.
  The content of this memory is addressable by location without regards to the contents.
  Execution occurs in sequential fashion
Notes: <number>

## Slide 5: What is a program?
A sequence of steps
For each step, an arithmetic or logical operation is done
For each operation, a different set of control signals is needed
The program interpreted by control unit as sequence of control signals is called the software
Notes: <number>

## Slide 6: Function of Control Unit
For each operation a unique code is provided
  e.g. ADD, MOVE
A hardware segment accepts the code and issues the control signals
We have a computer!
Notes: <number>

## Slide 7: Components
The Control Unit and the Arithmetic and Logic Unit constitute the Central Processing Unit
Data and instructions need to get into the system and results out
  Input/output
Temporary storage of code and results is needed
  Main memory
Notes: <number>

## Slide 8: Computer Components: Top Level View
Notes: <number>

## Slide 9: Instruction Cycle
Two steps:
  Fetch
  Execute
Notes: <number>

## Slide 10: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction and performs required actions
Notes: <number>

## Slide 11: Instruction Action Categories
Processor-memory
  data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above can be held by single instruction
Notes: <number>

## Slide 12: Instructions and Data Format
As simple example, consider hypothetical machine that holds data and instructions in a words of 16 bit length (2 bytes).
4 bits are used to hold the operation code (Opcode), allows up to 16 different operations 24.
Numbers are represented sign-magnitude format
Opcode
Address/Operand
0
15
4
3

## Slide 13: Example of Program Execution
Notes: <number>

## Slide 14: Instruction Cycle State Diagram
Notes: <number>

## Slide 15: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error
Notes: <number>

## Slide 16: Interrupts

## Slide 17: Count…

## Slide 19: Program Flow Control
Notes: <number>

## Slide 20: Transfer of Control via Interrupts

## Slide 21: Instruction Cycle (with Interrupts) - State Diagram
Notes: <number>

## Slide 22: Multiple Interrupts
Disable interrupts
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt
Notes: <number>

## Slide 23: Multiple Interrupts - Sequential
Notes: <number>

## Slide 24: Multiple Interrupts – Nested
Notes: <number>

## Slide 25: Time Sequence of Multiple Interrupts

## Slide 26: Connecting
All the units must be connected
Different type of connection for different type of unit
  Memory
  Input/Output
  CPU
Notes: <number>

## Slide 27: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing
Notes: <number>

## Slide 28: Input/Output Connection(1)
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer
Notes: <number>

## Slide 29: Input/Output Connection(2)
Receive control signals from computer
Send control signals to peripherals
  e.g. spin disk
Receive addresses from computer
  e.g. port number to identify peripheral
Send interrupt signals (control)
Notes: <number>

## Slide 30: Buses
There are a number of possible interconnection systems
Single and multiple BUS structures are most common
e.g. Control/Address/Data bus (PC)
e.g. Unibus (DEC-PDP)
Notes: <number>

## Slide 31: What is a Bus?
A communication pathway connecting two or more devices
Usually broadcast
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
Power lines may not be shown
Notes: <number>

## Slide 32: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit
Notes: <number>

## Slide 33: Address bus
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space
Notes: <number>

## Slide 34: Control Bus
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals
Notes: <number>

## Slide 35: Bus Interconnection Scheme
Notes: <number>

## Slide 36: Big and Yellow?
What do buses look like?
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
    e.g. PCI
  Sets of wires
Notes: <number>

## Slide 37: Physical Realization of Bus Architecture

## Slide 38: Single Bus Problems
Lots of devices on one bus leads to:
  Propagation delays
    Long data paths mean that co-ordination of bus use can adversely affect performance
    If aggregate data transfer approaches bus capacity
Most systems use multiple buses to overcome these problems
Notes: <number>

## Slide 39: Traditional (ISA) (with cache)
Notes: <number>

## Slide 40: High Performance Bus
Notes: <number>

## Slide 41: Bus Types
Dedicated
  Separate data & address lines
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Ultimate performance
Notes: <number>

## Slide 42: Centralised or Distributed Arbitration
Centralised
  Single hardware device controlling bus access
    Bus Controller
    Arbiter
  May be part of CPU or separate
Distributed
  Each module may claim the bus
  Control logic on all modules
Notes: <number>

## Slide 43: Timing
Co-ordination of events on bus
Synchronous
  Events determined by clock signals
  Control Bus includes clock line
  A single 1-0 is a bus cycle
  All devices can read clock line
  Usually sync on leading edge
  Usually a single cycle for an event
Notes: <number>

## Slide 44: Synchronous Timing Diagram
Notes: <number>

## Slide 45: Asynchronous Timing – Read Diagram
Notes: <number>

## Slide 46: Asynchronous Timing – Write Diagram

## Slide 47: PCI Read Timing Diagram
Notes: <number>

## Slide 48: PCI Bus Arbiter