## Slide 1: William Stallings Computer Organization and Architecture 7th Edition
Chapter 4
Cache Memory
Notes: <number>

## Slide 2: Characteristics
Location
Capacity
Unit of transfer
Access method
Performance
Physical type
Physical characteristics
Organisation
Notes: <number>

## Slide 3: Location
Whether the memory relative to CPU is
  Internal: the main memory, registers and cache all are kind of internal memories
  External: peripheral storage device such as disk and tape. They are accessible to CPU via device controller.
Notes: <number>

## Slide 4: Capacity
Word size
  For internal memory, this is expressed in bytes or words. The common word length is 8, 16, 32 or 64 bits
  The word is the natural unit of organisation, and is equal to the number of bits to represent instruction (some times there is exceptions for that).
Number of words
  or Bytes
Notes: <number>

## Slide 5: Unit of Transfer
Internal
  Usually governed by data bus width
External
  Usually a block which is much larger than a word
Addressable unit
  Smallest location which can be uniquely addressed
  Word internally
  Cluster on M$ disks
Notes: <number>

## Slide 6: Access Methods (1)
Sequential
  Start at the beginning and read through in order
  Access time depends on location of data and previous location
  e.g. tape
Direct
  Individual blocks have unique address
  Access is by jumping to vicinity plus sequential search
  Access time depends on location and previous location
  e.g. disk
Notes: <number>

## Slide 7: Access Methods (2)
Random
  Individual addresses identify locations exactly
  Access time is independent of location or previous access
  e.g. RAM
Associative
  Data is located by a comparison with contents of a portion of the store
  Access time is independent of location or previous access
  e.g. cache
Notes: <number>

## Slide 8: Memory Hierarchy
Registers
  In CPU
Internal or Main memory
  May include one or more levels of cache
  “RAM”
External memory
  Backing store
Notes: <number>

## Slide 9: Memory Hierarchy - Diagram

## Slide 10: Performance
Access time
  Time between presenting the address and getting the valid data
Memory Cycle time
  Time may be required for the memory to “recover” before next access.
  This time allow transient of the line signal to die (damping), or to regenerate data if they read destructively.
  Cycle time is access + recovery
Transfer Rate
  Rate at which data can be moved
Notes: <number>

## Slide 11: Physical Types
Semiconductor
  RAM
Magnetic
  Disk & Tape
Optical
  CD & DVD
Others
  Bubble
  Hologram
Notes: <number>

## Slide 12: Physical Characteristics
Decay
Volatility
Erasable
Power consumption
Notes: <number>

## Slide 13: Organisation
Physical arrangement of bits into words
Not always obvious
e.g. interleaved
Notes: <number>

## Slide 14: The Bottom Line
How much?
  Capacity
How fast?
  Time is money
How expensive?
Notes: <number>

## Slide 15: Hierarchy List
Registers
L1 Cache
L2 Cache
Main memory
Disk cache
Disk
Optical
Tape
Notes: <number>

## Slide 16: So you want fast?
It is possible to build a computer which uses only static RAM (see later)
This would be very fast
This would need no cache
  How can you cache cache?
This would cost a very large amount
Notes: <number>

## Slide 17: Locality of Reference
During the course of the execution of a program, memory references tend to cluster
e.g. loops
Notes: <number>

## Slide 18: Cache
Small amount of fast memory to improve the performance with cheap price.
Sits between normal main memory and CPU to keep part of the data and instructions in the main memory.
May be located on CPU chip or module
Notes: <number>

## Slide 19: Cache
Hit: when the processor fetch word and find it in the cache, otherwise Miss occurs.
If miss occurs the block of the required word (consists of fixed number of words) is read from main memory and saved in the cache.
Because of the locality principle, it likely to find the next referenced data or instructions in the cache as result of binging the whole block rather than the required word.

## Slide 20: Cache
Memory of size 2n will have n address lines.
The main memory is divided into blocks ,each block consists of k words (i.e. the number of blocks M = 2n/k .
The cache consists of lines C , each has the same size as block and C << M.
At any time the cache will holds some blocks which are involved with processor work at that time.
As the number of C is much less than the number of blocks, each line will have tag to indicate the block it holds.

## Slide 21: Cache/Main Memory Structure

## Slide 22: Cache operation – overview
CPU requests contents of memory location
Check cache for this data
If present, get from cache (fast)
If not present, read required block from main memory to cache
Then deliver from cache to CPU
Cache includes tags to identify which block of main memory is in each cache slot
Notes: <number>

## Slide 23: Cache Read Operation - Flowchart

## Slide 24: Cache Design
Size
Mapping Function
Replacement Algorithm
Write Policy
Block Size
Number of Caches
Notes: <number>

## Slide 25: Size does matter
Cost
  More cache is more expensive
Speed
  More cache is faster (up to a point)
  Checking cache for data takes time
Notes: <number>

## Slide 26: Typical Cache Organization
Notes: <number>

## Slide 27: Comparison of Cache Sizes
a Two values seperated by a slash refer to instruction and data caches
b Both caches are instruction only; no data caches
Processor
Type
Year of Introduction
L1 cachea
L2 cache
L3 cache
IBM 360/85
Mainframe
1968
16 to 32 KB
—
—
PDP-11/70
Minicomputer
1975
1 KB
—
—
VAX 11/780
Minicomputer
1978
16 KB
—
—
IBM 3033
Mainframe
1978
64 KB
—
—
IBM 3090
Mainframe
1985
128 to 256 KB
—
—
Intel 80486
PC
1989
8 KB
—
—
Pentium
PC
1993
8 KB/8 KB
256 to 512 KB
—
PowerPC 601
PC
1993
32 KB
—
—
PowerPC 620
PC
1996
32 KB/32 KB
—
—
PowerPC G4
PC/server
1999
32 KB/32 KB
256 KB to 1 MB
2 MB
IBM S/390 G4
Mainframe
1997
32 KB
256 KB
2 MB
IBM S/390 G6
Mainframe
1999
256 KB
8 MB
—
Pentium 4
PC/server
2000
8 KB/8 KB
256 KB
—
IBM SP
High-end server/ supercomputer
2000
64 KB/32 KB
8 MB
—
CRAY MTAb
Supercomputer
2000
8 KB
2 MB
—
Itanium
PC/server
2001
16 KB/16 KB
96 KB
4 MB
SGI Origin 2001
High-end server
2001
32 KB/32 KB
4 MB
—
Itanium 2
PC/server
2002
32 KB
256 KB
6 MB
IBM POWER5
High-end server
2003
64 KB
1.9 MB
36 MB
CRAY XD-1
Supercomputer
2004
64 KB/64 KB
1MB
—

## Slide 28: Mapping Function
Cache of 64kByte
Cache block of 4 bytes
  i.e. cache is 16k (214) lines of 4 bytes
16MBytes main memory
24 bit address
  (224=16M)
Notes: <number>

## Slide 29: Direct Mapping
Each block of main memory maps to only one cache line
  i.e. if a block is in cache, it must be in one specific place
Address is in two parts
Least Significant w bits identify unique word (w depends on the block size)
Most Significant s bits specify one memory block
The MSBs are split into a cache line field r and a tag of s-r (most significant)
Notes: <number>

## Slide 30: Direct Mapping Address Structure
Tag s-r
Line or Slot r
Word w
8
14
2
24 bit address
2 bit word identifier (4 byte block)
22 bit block identifier
  8 bit tag (=22-14) [N.B. the no. of lines in the cache are 214= 16 K lines]
  14 bit slot or line
No two blocks in the same line have the same Tag field
Check contents of cache by finding line and checking Tag
Notes: <number>

## Slide 31: Direct Mapping Cache Line Table
Cache line Main Memory blocks held
0 0, m, 2m, 3m…2s-m
1 1,m+1, 2m+1…2s-m+1
m-1 m-1, 2m-1,3m-1…2s-1
Notes: <number>

## Slide 32: Direct Mapping Cache Organization
Notes: <number>

## Slide 33: Direct Mapping Example
Notes: <number>

## Slide 34: Direct Mapping Summary
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes
Block size = line size = 2w words or bytes
Number of blocks in main memory=2s+w/2w = 2s
Number of lines in cache = m = 2r
Size of tag = (s – r) bits

## Slide 35: Direct Mapping pros & cons
Simple
Inexpensive
Fixed location for given block
  If a program accesses 2 blocks that map to the same line repeatedly, cache misses are very high
Notes: <number>

## Slide 36: Associative Mapping
A main memory block can load into any line of cache
Memory address is interpreted as tag and word
Tag uniquely identifies block of memory
Every line’s tag is examined for a match
Cache searching gets expensive
Notes: <number>

## Slide 37: Fully Associative Cache Organization
Notes: <number>

## Slide 38: Associative Mapping Example
Notes: <number>

## Slide 39: Associative Mapping Address Structure
Tag 22 bit
Word
2 bit
22 bit tag stored with each 32 bit block of data
Compare tag field with tag entry in cache to check for hit
Least significant 2 bits of address to identify which 8 bit byte number is required from 32 bit data block
e.g.
  Address Tag Data Cache line
  FFFFFC 3FFFFF 24682468 3FFF
Notes: <number>

## Slide 40: Associative Mapping Summary
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes
Block size = line size = 2w words or bytes
Number of blocks in main memory = 2s+w/2w = 2s
Number of lines in cache = undetermined
Size of tag = s bits

## Slide 41: Set Associative Mapping
Cache is divided into a number of sets
Each set contains a number of lines
A given block maps to any line in a given set
  e.g. Block B can be in any line of set i
e.g. 2 lines per set
  2 way associative mapping
  A given block can be in one of 2 lines in only one set
Notes: <number>

## Slide 42: Set Associative Mapping Example
13 bit set number
Block number in main memory is modulo 213
000000, 00A000, 00B000, 00C000 … map to same set
Notes: <number>

## Slide 43: Two Way Set Associative Cache Organization
Notes: <number>

## Slide 44: Set Associative Mapping Address Structure
Use set field to determine cache set to look in
Compare tag field to see if we have a hit
e.g
  Address Tag Data Set number
  1FF 7FFC 1FF 12345678 1FFF
  001 7FFC 001 11223344 1FFF
Tag 9 bit
Set 13 bit
Word
2 bit
Notes: <number>

## Slide 45: Two Way Set Associative Mapping Example
Notes: <number>

## Slide 46: Set Associative Mapping Summary
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes
Block size = line size = 2w words or bytes
Number of blocks in main memory = 2s
Number of lines in set = k
Number of sets = v = 2d
Number of lines in cache = kv = k * 2d
Size of tag = (s – d) bits

## Slide 47: Set Associative Mapping Summary
If number of sets (v) = number of lines (m) [i.e. number of lines for each set k=1], the set associative technique will convert to direct mapping.
If k=m, v=1 (set associative will be fully associative)
The most common choice (v=m/2 and k=2).
Four way set associative means (k= 4 and v=v/4).

## Slide 48: Replacement Algorithms (1) Direct mapping
No choice
Each block only maps to one line
Replace that line
Notes: <number>

## Slide 49: Replacement Algorithms (2) Associative & Set Associative
Hardware implemented algorithm (speed)
Least Recently used (LRU): replace the line stayed in memory longest time with no reference.
e.g. in 2 way set associative
  Which of the 2 block is LRU? (use bit)
First in first out (FIFO) (
  replace block that has been in cache longest and is implemented as R.R.
Least frequently used
  replace block which has had fewest hits
Random (implemented using counter)
Notes: <number>

## Slide 50: Write Policy
A cache line must not overwritten by a block unless main memory is up to date
Multiple CPUs may have individual caches
I/O may address main memory directly and it may cause inconsistency.
Notes: <number>

## Slide 51: Write through
All writes go to main memory as well as cache
Multiple CPUs can monitor main memory traffic to keep local (to CPU) cache up to date
Lots of traffic
Slows down writes
Remember bogus write through caches!
Notes: <number>

## Slide 52: Write back
Updates initially made in cache only
Update bit for cache slot is set when update occurs
If block is to be replaced, write to main memory only if update bit is set
Other caches get out of sync
I/O must access main memory through cache
N.B. 15% of memory references are writes
Notes: <number>

## Slide 53: Cache Coherency
Many devices (Normally CPU’s) have caches and all are sharing memory
Solutions:
Bus watching with write through
Hardware transparency: in which special hardware is used to reflect any modification in cache to memory and all other caches.
Non cacheable memory: a portion in memory only is shared and this is not allowed to be cached. (i.e. all reference to this part is causing Miss). Hardware can identify the non cacheable memory (CS).

## Slide 54: Pentium 4 Cache
80386 – no on chip cache
80486 – 8k using 16 byte lines and four way set associative organization
Pentium (all versions) – two on chip L1 caches
  Data & instructions
Pentium III – L3 cache added off chip
Pentium 4
  L1 caches
    8k bytes
    64 byte lines
    four way set associative
  L2 cache
    Feeding both L1 caches
    256k
    128 byte lines
    8 way set associative
  L3 cache on chip
Notes: <number>

## Slide 55: Line Size
As the block size increases initially the hit ratio will increase until certain point at which the hit ratio is decreasing.
Larger block reduces the number of blocks that fit into cache contents. A small number of blocks results data to be written shortly after they are fetched.
Each additional word in large block will be less likely to be used.

## Slide 56: Number of Caches
Single cache is found initially and with increasing chip density became available some space for on-chip cache.
The system benefits from that by reducing external bus activity (speeds up the execution time).
Because the bus of the on-chip cache is shorter than the system bus as result of few devices are connected to it, the on-chip bus is faster (less delay).
During this period of using on-chip cache the system bus will be avialable for other activities.

## Slide 57: Is still the external cache desirable?
Shortly, the answer is yes and this organization is called two level cache.
Internal cache is L1 and the external cache is L2.
With no L2 cache (SRAM), in case of MISS the CPU has to access the RAM or ROM directly through the system bus (slow, and performance decreasing).
Many systems are using separate bus between L2 and the processor to reduce burden on the system bus.
The continuous shrinking of the processor components, many system place L2 on the processor chip (impoving the performance).

## Slide 58: Unified against Split cache
At start L1 cache is used for both of data and instruction.
Recently become common to split cache into one for data and the one for instructions.
  Reason for modified cache are:
  For specific size it will have higher Hit rate (as result of balancing data and instructions automatically).
  Only one cache has to implemented and design.

## Slide 59: Unified against Split cache
Split caches, eliminate contention particularly for supper scalar processor (PowerPC and Pentium) which emphasis parallel instruction and pre-fetching of predicted future instructions. This is very important for any design depends on pipelining.

## Slide 60: Intel Cache Evolution
Problem
Solution
Processor on which feature first appears
External memory slower than the system bus.
Add external cache using faster memory technology.
386
Increased processor speed results in external bus becoming a bottleneck for cache access.
Move external cache on-chip, operating at the same speed as the processor.
486
Internal cache is rather small, due to limited space on chip
Add external L2 cache using faster technology than main memory
486
Contention occurs when both the Instruction Prefetcher and the Execution Unit simultaneously require access to the cache. In that case, the Prefetcher is stalled while the Execution Unit’s data access takes place.
Create separate data and instruction caches.
Pentium
Increased processor speed results in external bus becoming a bottleneck for L2 cache access.
Create separate back-side bus that runs at higher speed than the main (front-side) external bus. The BSB is dedicated to the L2 cache.
Pentium Pro
Move L2 cache on to the processor chip.
Pentium II
Some applications deal with massive databases and must have rapid access to large amounts of data. The on-chip caches are too small.
Add external L3 cache.
Pentium III
Move L3 cache on-chip.
Pentium 4

## Slide 61: Pentium 4 Block Diagram

## Slide 62: Pentium 4 Core Processor
Fetch/Decode Unit
  Fetches instructions from L2 cache
  Decode into micro-ops
  Store micro-ops in L1 cache
Out of order execution logic
  Schedules micro-ops
  Based on data dependence and resources
  May speculatively execute
Execution units
  Execute micro-ops
  Data from L1 cache
  Results in registers
Memory subsystem
  L2 cache and systems bus

## Slide 63: Pentium 4 Design Reasoning
Decodes instructions into RISC like micro-ops before L1 cache
Micro-ops fixed length
  Superscalar pipelining and scheduling
Pentium instructions long & complex
Performance improved by separating decoding from scheduling & pipelining
  (More later – ch14)
Data cache is write back
  Can be configured to write through
L1 cache controlled by 2 bits in register
  CD = cache disable
  NW = not write through
  2 instructions to invalidate (flush) cache and write back then invalidate
L2 and L3 8-way set-associative
  Line size 128 bytes

## Slide 64: PowerPC Cache Organization
601 – single 32kb 8 way set associative
603 – 16kb (2 x 8kb) two way set associative
604 – 32kb
620 – 64kb
G3 & G4
  64kb L1 cache
    8 way set associative
  256k, 512k or 1M L2 cache
    two way set associative
G5
  32kB instruction cache
  64kB data cache

## Slide 65: PowerPC G5 Block Diagram

## Slide 66: Internet Sources
Manufacturer sites
  Intel
  IBM/Motorola
Search on cache